## Slide 1: Advanced Computer Architecture
Prof. Moinuddin Qureshi
Thanks to Prof. Kim, Prof. Loh, Prof. Pruvulovic for earlier versions of the lecture notes!

## Slide 2: Memory Hierarchy
Memory: Just an “ocean of bits”
IDEAL Memory: Zero cost, zero latency, infinite capacity
Trade-off between: latency and capacity (big is slow)
Trade-off between cost: fast is typically expensive
Solution: Build a hierarchy (frequent: fast, else: slow, cheap)

## Slide 3: Memory Hierarchy
Registers
On-Chip
SRAM
Off-Chip
SRAM
DRAM
Flash/Disk
CAPACITY
SPEED and COST

## Slide 4: Locality and Caches
Data Locality
  Temporal: if data item needed now, it is likely to be needed again in near future
  Spatial: if data item needed now, nearby data likely to be needed in near future
Exploiting Locality: Caches
  Keep recently used data in fast memory close to the processor
  Also bring nearby data there

## Slide 5: Memory Latency is Long
60-100ns not uncommon
Quick back-of-the-envelope calculation:
  2GHz CPU
   0.5ns / cycle
  100ns memory  200 cycle memory latency!
Solution: Caches

## Slide 6: Cache Basics
Fast (but small) memory close to processor
When data referenced
  If in cache, use cache instead of memory
  If not in cache, bring into cache (actually, bring entire block of data, too)
  Maybe have to kick something else out to do it!
Important decisions
  Placement: where in the cache can a block go?
  Identification: how do we find a block in cache?
  Replacement: what to kick out to make room in cache?
  Write policy: What do we do about stores?
Key: Optimize the
average memory
access latency

## Slide 7: Review questions
Memory addresses A, A+1, A+2, A+3, A+4
  Spatial locality or temporal locality?:
  Spatial locality
Memory addresses A, B,C, A,B,C,A,B,C
  Spatial locality or temporal locality?
  Temporal locality

## Slide 8: Cache Basics: A Layman View
Consider a library in law dept.: many books, each 100 pages.
Pages identified with [BOOKNAME][PAGENUM]
eg. MYBOOK64, OLDBOOK75, FINES88
We have a shelf that can store 2600 pages or 26 Books
How to organize this shelf?

## Slide 9: Cache Basics: A Layman View
Perhaps we want to keep books instead of individual pages  -Less book-keeping overhead
-Likely we read many pages from same book
26 Books. Need to check quickly if book in my shelf
How about partitioning the shelf? Hashing based on first char
What is the problem? Can’t hold two books starting with “A”
How about below: 13 bins (each with two places  flexibility)
A | B | C | D | E | F | G | H | I | J | K | L | M | N | O | P | Q | R | S | T | U | V | W | X | Y | Z
A or B
Y or Z

## Slide 10: Cache Basics
Cache consists of block-sized lines
  Line size typically power of two
  Typically 16 to 256 bytes in size
Example
  Suppose block size is 256 bytes
    Lowest eight bits determine offset within block
  Read data at address A=0xFADEDACE
  The block address is 0xFADEDA,
  Byte in block is 0xCE
MSB
LSB
Block size

## Slide 11: Cache Placement
Placement
  Which memory blocks are allowed into which cache lines
Placement Policies
  Direct mapped (block can go to only one line)
  Fully Associative (block can go to any line)
  Set-associative (block can go to one of N lines)
    E.g., if N=4, the cache is 4-way set associative
    Other two policies are extremes of this (E.g., if N=1 we get a direct-mapped cache)

## Slide 12: Cache Identification
When address referenced, need to
  Find whether its data is in the cache
  If it is, find where in the cache
  This is called a cache lookup
Each cache line must have
  A valid bit (1 if line has data, 0 if line empty)
    We also say the cache line is valid or invalid
  A tag to identify which block is in the line (if line is valid)

## Slide 13: Index
dex
Index
TAG
Block offset
TAG
TAG
=
=
HIT
YES
YES
Data
Logic
Pop quiz: Why is index typically the least significant bits (LSBs) and not MSBs

## Slide 14: Parallel/Serial TAG and Data Array Access
Synthesis lecture series: microarchitecture

## Slide 15: Cache Replacement
Need a free line to insert new block
  Which block should we kick out?
Several strategies
  Random (randomly selected line)
  FIFO (line that has been in cache the longest)
  LRU (least recently used line)
  LRU Approximations (Pseudo LRU)

## Slide 16: Implementing LRU
Have “time-stamp” with each line  Expensive
Maintain a LRU “stack”
  Ordered list with MRU line on top, LRU line on bottom
  On a hit, remove the line from list and put on top of stack
  For eviction, select line from bottom
Stack Algorithm still needs Log2(Assoc) bits per line
LRU approximations: Clock (1-bit LRU), NMRU, Tree etc.

## Slide 17: Review questions-II
Here is a series of address references given as word address: 1,4,8,5,20,17,19,56,9,11,4,4,3,5,6,9,17. Assuming a direct-mapped cache with 16 one-word blocks that is initially empty, label each reference in the list as a hit or miss and show the final contents of the cache.
1%16 =1
4%16 = 4
8%16 =8
5%16 =5
20%16 = 4
17%16 = 1
19%16 =3
56%16 = 8
9%16 =9
11%16 =11
4%16 = 4
4% 16 = Hit
3 % 16 = 3
5%16 = 5 Hit
6%16 = 6
9%16 = 9 Hit
17%16 =1 Hit
0 | 
1 | 1 17
2 | 
3 | 19 3
4 | 4 20 4
5 | 5
6 | 6
7 | 
8 | 8 56
9 | 9
10 | 
11 | 11 43
12 | 
13 | 
14 | 
15 | 

## Slide 18: Write Policy
Do we allocate cache lines on a write?
  Write-allocate
    A write miss brings block into cache
  No-write-allocate
    A write miss leaves cache as it was
  Pros and cons?
    Depends on temporal locality
Do we update memory on writes?
  Write-through
    Memory immediately updated on each write
  Write-back
    Memory updated when line replaced

## Slide 19: Write Through/Write Back
PROC
CACHE
MEM
PROC
CACHE
MEM
  Write-through
  Write-back
replacement

## Slide 20: Write-Back Caches
Need a Dirty bit for each line (stored in the Tag!)
  A dirty line has more recent data than memory
Line starts as clean (not dirty)
Line becomes dirty on first write to it
  Memory not updated yet, cache has the only up-to-date copy of data for a dirty line
Replacing a dirty line
  Must write data back to memory (write-back)

## Slide 21: Tag Storage
Any information related to cache other than data is stored in the tag storage.
Not only tag bits, information for replacement, dirty bits (if we need), valid bit
(in the future, cache coherence state information)

## Slide 22: TAG
Offset: Byte offset in block
Index: Which set in the cache is the block located
Tag: need to match address tag in cache
Set: Group of blocks corresponding to same index
MSB
LSB
Offset
Index
TAG
Data
address

## Slide 23: Cache Performance
Miss rate
  Fraction of memory accesses that miss in cache
  Hit rate = 1 – miss rate
Average memory access time
  AMAT = hit time + miss rate * miss penalty
Memory stall cycles
CPUtime = CycleTime x (CyclesExec + CyclesMemoryStall)
CyclesMemoryStall = CacheMisses x (MissLatencyTotal – MissLatencyOverlapped)

## Slide 24: Improving Cache Performance
AMAT = hit time + miss rate * miss penalty
  Reduce miss penalty
  Reduce miss rate
  Reduce hit time
CyclesMemoryStall = CacheMisses x (MissLatencyTotal – MissLatencyOverlapped)
  Increase overlapped miss latency
  Increase memory level parallelism

## Slide 25: Improving Cache Performance (2)
Memory latency = 100 cycles
16KB cache, 3 cycle latency, 85% hit rate
What’s the baseline AMAT?
= 3+100*0.15 = 18
What’s the best way to reduce latency?
  Smaller 8KB cache: 1 cycle latency, 75% hit rate
  = 1+ 100*0.25 = 26
  Larger 32KB cache: 4 cycle latency, 90% hit rate
  = 4 + 100*0.1 = 14

## Slide 26: Reducing Cache Miss Penalty (1)
Multilevel caches
  Very Fast, small Level 1 (L1) cache
  Fast, not so small Level 2 (L2) cache
  May also have slower, large L3 cache, etc.
Why does this help?
  Miss in L1 cache can hit in L2 cache, etc.
    AMAT = HitTimeL1+MissRateL1MissPenaltyL1
    MissPenaltyL1= HitTimeL2+MissRateL2MissPenaltyL2
    MissPenaltyL2= HitTimeL3+MissRateL3MissPenaltyL3

## Slide 27: Multi-Level Caches
Memory latency = 100 cycles
16KB L1 cache, 3 cycle latency, 85% hit rate
Use two levels of caching
  Smaller 8KB cache: 1 cycle latency, 75% hit rate
  Larger 128KB cache: 6 cycle latency, 60% hit rate
Exclusion Property
  If block is in L1 cache, it is never in L2 cache
  Saves some L2 space
Inclusion Property
  If block A is in L1 cache, it must also be in L2 cache

## Slide 28: Reducing Cache Miss Penalty (2)
Early Restart & Critical Word First
  Block transfer takes time (bus too narrow)
  Give data to loads before entire block arrive
Early restart
  When needed word arrives, let processor use it
  Then continue block transfer to fill cache line
Critical Word First
  Transfer loaded word first, then the rest of block (with wrap-around to get the entire block)
  Use with early restart to let processor go ASAP

## Slide 29: Reducing Cache Miss Penalty (3)
Increase Load Miss Priority
  Loads can have dependent instructions
  If a load misses and a store needs to go to memory, let the load miss go first
  Need a write buffer to remember stores
Merging Write Buffer
  If multiple write misses to the same block, combine them in the write buffer
  Use block-write instead of a many small writes

## Slide 30: Kinds of Cache Misses
The “3 Cs”
  Compulsory: have to have these
    Miss the first time each block is accessed
  Capacity: due to limited cache capacity
    Would not have them if cache size was infinite
  Conflict: due to limited associativity
    Would not have them if cache was fully associative

## Slide 31: Loop Interchange
For loops over multi-dimensional arrays
  Example: matrices (2-dim arrays)
Change order of iteration to match layout
  Gets better spatial locality
  Layout in C: last index changes first
for(j=0;j<10000;j++) for(i=0;i<40000;i++) c[i][j]=a[i][j]+b[i][j];
for(i=0;i<40000;i++) for(j=0;j<10000;j++) c[i][j]=a[i][j]+b[i][j];
a[i][j] and a[i+1][j] are 10000 elements apart
a[i][j] and a[i][j+1] are next to each other

## Slide 32: Review
Improving cache performance
  Cache block sizes?
  Cache write polices?
  Multi-level caches
  Inclusion/exclusion property
  Write buffers

## Slide 33: Question
#define MAX_LAST_NAME_SIZE 16
typedef struct _TAGPHONE_BOOK_ENTRY {
  char LastName[MAX_LAST_NAME_SIZE];
  char FirstNAME[16]; char email[16]; char phone[10]; char cell[10]; char addr1[16];
  char addr2[16]; char city[16]; char state[2]; char zip[5];
  _TAGPHONE_BOOK_ENTRY *pNext;
  } Phone BOOK
  PhoneBook *FindName(char Last[], PhoneBook *pHead) {
  While (pHead != NULL) {
  if (stricmp (Last, pHead->LastName) == 0)
  Return pHead;
  pHead = pHead->pNext;
  }
  return NULL;
  }
What are the problems and how to improve the cache locality?

## Slide 34: Solutions
Among 127 B, only 20B are used.
Cache block size is 64B
(1) Rearrange the data structure (Put LastName & Pointers nearby)
(2) Put all LastName together and then put the rest of them somewhere
127B
Last Name
Pointer
Last Name
Pointer
Last Name
Last Name
Last Name

## Slide 35: Hiding Miss Latency
Idea: overlap miss latency with useful work
  Also called “latency hiding”
Non-blocking (Lockup-free) caches
  A blocking cache services one access at a time
    While miss serviced, other accesses blocked (wait)
  Non-blocking caches remove this limitation
    While miss serviced, can process other requests
Prefetching
  Predict what will be needed and get it ahead of time

## Slide 36: Non-Blocking (Lockup-Free) Caches
Hit Under Miss
  Allow cache hits while one miss in progress
  But another miss has to wait
Miss Under Miss, Hit Under Multiple Misses
  Allow hits and misses when other misses in progress
  Memory system must allow multiple pending requests
MSHR (Miss Information/Status Holding Register): Stores unresolved miss information for each miss that will be handled concurrently.

## Slide 37: MSHR (Miss Status Holding Register)
Track address, data, and status for multiple outstanding cache misses
Provide correct memory ordering, other information (e.g, cache coherence)
Valid flag,
Write bits
# of entries: # of outstanding memory requests

## Slide 38: Example
Miss A
Miss B
Inst1: LD Block A (cache miss)
Inst2: LD Block B (cache miss)
If Blocking Cache
If Non-Blocking Cache
Miss A
Miss B
Saved Cycles