## Slide 1: ECE4100/ECE6100/CS4290/CS6290
Thanks to Prof. Kim, Prof. Loh & Prof. Prvulovic

## Slide 2: Problem
P2
P1
$
Main Memory
A1: 10
A2: 20
A3: 39
A4: 17
P1
P3
$
$
ST MEM[A1] 20
A1: 20
LD MEM[A1]
LD MEM[A1]
A1: 10
10 ? 20

## Slide 3: Cache Coherence Problem
Shared memory easy with no caches
  P1 writes, P2 can read
  Only one copy of data exists (in memory)
Caches store their own copies of the data
  Those copies can easily get inconsistent
  Classic example: adding to a sum
    P1 loads allSum, adds its mySum, stores new allSum
    P1’s cache now has dirty data, but memory not updated
    P2 loads allSum from memory, adds its mySum, stores allSum
    P2’s cache also has dirty data
    Eventually P1 and P2’s cached data will go to memory
    Regardless of write-back order, the final value ends up wrong

## Slide 4: Cache Coherence Definition
A memory system is coherent if
  A read R from address X on processor P1 returns the value written by the most recent write W to X on P1 if no other processor has written to X between W and R.
  If P1 writes to X and P2 reads X after a sufficient time, and there are no other writes to X in between, P2’s read returns the value written by P1’s write.
  Writes to the same location are serialized: two writes to location X are seen in the same order by all processors.

## Slide 5: Cache Coherence Definition
Property 1. preserves program order
  It says that in the absence of sharing, each processor behaves as a uniprocessor would
Property 2. says that any write to an address must eventually be seen by all processors
  If P1 writes to X and P2 keeps reading X, P2 must eventually see the new value
Property 3. preserves causality
  Suppose X starts at 0. Processor P1 increments X and processor P2 waits until X is 1 and then increments it to 2. Processor P3 must eventually see that X becomes 2.
  If different processors could see writes in different order, P2 can see P1’s write and do its own write, while P3 first sees the write by P2 and then the write by P1. Now we have two processors that will forever disagree about the value of A.

## Slide 6: SNOOPING
P2
P1
$
Main Memory
A1: 10
A2: 20
A3: 39
A4: 17
P1
P3
$
$
A1: 20
LD MEM[A1]
A1: 20

## Slide 7: SNOOPING
P2
P1
$
Main Memory
A1: 20
A2: 20
A3: 39
A4: 17
P1
P3
$
$
A1: 20
ST MEM[A2]
A1: 20
A2: 30
A2: 40
A2: 50
A2: 60

## Slide 8: Snooping
Typically used for bus-based (SMP) multiprocessors
  Serialization on the bus used to maintain coherence property 3
Two flavors
  Write-update (write broadcast)
    A write to shared data is broadcast to update all copies
    All subsequent reads will return the new written value (property 2)
    All see the writes in the order of broadcasts One bus == one order seen by all (property 3)
  Write-invalidate
    Write to shared data forces invalidation of all other cached copies
    Subsequent reads miss and fetch new value (property 2)
    Writes ordered by invalidations on the bus (property 3)

## Slide 9: Update vs. Invalidate
A burst of writes by a processor to one addr
  Update: each sends an update
  Invalidate: possibly only the first invalidation is sent
Writes to different words of a block
  Update: update sent for each word
  Invalidate: possibly only the first invalidation is sent
Producer-consumer communication latency
  Update: producer sends an update, consumer reads new value from its cache
  Invalidate: producer invalidates consumer’s copy, consumer’s read misses and has to request the block
Which is better depends on application
  But write-invalidate is simpler and implemented in most MP-capable processors today

## Slide 10: MSI Snoopy Protocol
State of block B in cache C can be
  Invalid: B is not cached in C
    To read or write, must make a request on the bus
  Modified: B is dirty in C
    has the block, no other cache has the block, and C must update memory when it displaces B
    Can read or write B without going to the bus
  Shared: B is clean in C
    C has the block, other caches have the block, and C need not update memory when it displaces B
    Can read B without going to bus
    To write, must send an upgrade request to the bus

## Slide 11: MSI Example
P2
P1
$
Main Memory
A1: 10
A2: 20
A3: 39
A4: 17
P1
P3
$
$
ST MEM[A1] 20
A1: 20
LD MEM[A1]
A1: 10
M
Cache Miss
Cache Miss
Hit
A1: 20
A1: 20
S
S
ST MEM[A1] 30
A1:30
M
I

## Slide 12: MSI
I
S
M
Fill out CPU read, CPU write
BUS read, BUS write

## Slide 13: MSI
I
S
M
cpu read
cpu write
cpu write
cpu read
cpu read/write
Bus write
Bus read
Bus read
Bus write
Bus read/write

## Slide 14: MSI Snoopy Protocol
My RD/WR:
My action
Someone else
Also called “modified”

## Slide 15: Review Question
MSI protocol : cache block size is 4B
  P1 LDB mem[A]
  P2 STB mem[A]
  P3 LDB mem[A]
  P1 STB mem[A]
  P2 STB mem[A]
  P3 LDB mem[A]
P1 | P2 | P3
S | X | X
I | M | X
I | S | S
M | I | I
I | M | I
I | S | S

## Slide 16: Cache to Cache Transfers
Problem
  P1 has block B in M state
  P2 wants to read B, puts a RdReq on bus
  If P1 does nothing, memory will supply the data to P2
  What does P1 do?
Solution 1: abort/retry
  P1 cancels P2’s request, issues a write back
  P2 later retries RdReq and gets data from memory
  Too slow (two memory latencies to move data from P1 to P2)
Solution 2: intervention
  P1 indicates it will supply the data (“intervention” bus signal)
  Memory sees that, does not supply the data, and waits for P1’s data
  P1 starts sending the data on the bus, memory is updated
  P2 snoops the transfer during the write-back and gets the block

## Slide 17: Cache-To-Cache Transfers
Intervention works if some cache has data in M state
  Nobody else has the correct data, clear who supplies the data
What if a cache has requested data in S state
  There might be others who have it, who should supply the data?
  Solution 1: let memory supply the data
  Solution 2: whoever wins arbitration supplies the data
  Solution 3: A separate state similar to S that indicates there are maybe others who have the block in S state, but if anybody asks for the data we should supply it

## Slide 18: Illinois’ Protocol (MESI)
I
S
M
cpu read, shared
cpu write
cpu write
(write through)
cpu read
cpu read/write
Bus write
Bus read
Bus read
Bus write
Bus read/write
E
cpu read
cpu write
(write back)
Bus write
Bus read
cpu read, exclusive

## Slide 19: MESI Protocol (Alternative Version)
I
S
M
cpu read, shared
cpu write
cpu write
cpu read
cpu read/write
Bus write
Bus read
Bus read
Bus write
Bus read/write
E
cpu read
cpu write
(write back)
Bus write
Bus read
cpu read, exclusive

## Slide 20: MESI Protocol
New state: exclusive
  data is clean
  but I have the only copy (except memory)
Benefit: bandwidth reduction
  No broadcasting from E M because I have copy

## Slide 21: MESI Question
MESI protocol : cache block size is 4B
  P1 LDB mem[A]
  P1 STB mem[A]
  P3 LDB mem[A]
  P1 STB mem[A]
  P2 STB mem[A]
  P2 STB mem[A]
  P3 LDB mem[A]
P1 | P2 | P3
E | X | X
M | X | X
S | X | S
M | X | I
I | M | I
I | M | I
I | S | S

## Slide 22: MOESI
M: Modified (dirty, unique)
  I have the only copy, and it’s dirty (memory is stale)
O: Owned (dirty, shared)
  I have the most up-to-date copy, others may have copies, too, but I am responsible for sourcing data
E: Exclusive (clean, unique)
  I have the only copy (clean)
S: Shared (clean, shared)
  Everyone has a clean copy (incl. memory)
I: Invalid

## Slide 23: Directory-Based Coherence
Typically in distributed shared memory
For every local memory block, local directory has an entry
Directory entry indicates
  Who has cached copies of the block
  In what state do they have the block

## Slide 24: Basic Directory Scheme
Each entry has
  One dirty bit (1 if there is a dirty cached copy)
  A presence vector (1 bit for each node) Tells which nodes may have cached copies
All misses sent to block’s home
Directory performs needed coherence actions
Eventually, directory responds with data

## Slide 25: Distributed MSI Example
CPU0
cache
Dist.Memory0
CPU1
cache
CPU2
cache
CPU3
cache
Dist.Memory1
Dist.Memory2
Dist.Memory3
Interconnection Network
Add 0-0x1000
Add 0x1000-0x2000
Add 0x2000-0x3000
Add 0x3000-0x4000

## Slide 26: Read Miss
Processor Pk has a read miss on block B, sends request to home node of the block
Directory controller
  Finds entry for B, checks D bit
  If D=0
    Read memory and send data back, set P[k]
  If D=1
    Request block from processor whose P bit is 1
    When block arrives, update memory, clear D bit, send block to Pk and set P[k]

## Slide 27: Directory Operation
Network controller connected to each bus
  A proxy for remote caches and memories
    Requests for remote addresses forwarded to home, responses from home placed on the bus
    Requests from home placed on the bus, cache responses sent back to home node
Each cache still has its own coherence state
  Directory is there just to avoid broadcasts and order accesses to each location
    Simplest scheme: If access A1 to block B still not fully processed by directory when A2 arrives, A2 waits in a queue until A1 is done

## Slide 28: Shared Memory Performance
Another “C” for cache misses
  Still have Compulsory, Capacity, Conflict
  Now have Coherence, too
    We had it in our cache and it was invalidated
Two sources for coherence misses
  True sharing
    Different processors access the same data
  False sharing
    Different processors access different data, but they happen to be in the same block

## Slide 29: False Sharing
X and Y are in the same cache block, P1 and P2 are read/write X & Y
time | P1 | P2 | Cache hit,miss ? /Coherence state (P1, P2) [M,S,I]
1 | Read X |  | Miss (S, X)
2 |  | Read X | Miss (S,S)
3 | Write X |  | Hit (M, I)
4 |  | Read X | Miss (S, S)
time | P1 | P2 | Cache hit,miss ? (P1,P2)
1 | Read X |  | Miss (S,X)
2 |  | Read Y | Miss (S,S)
3 | Write X |  | Hit (M, I)
4 |  | Read Y | Miss (S,S)
True Sharing
False Sharing