## Slide 1: Graphics Processing Units SIMD not Exposed to Programmer (SIMT)

## Slide 2: Concept of “Thread Warps” and SIMT
Warp: A set of threads that execute the same instruction (on different data elements)  SIMT (Nvidia-speak)
All threads run the same kernel
Warp: The threads that run lengthwise in a woven fabric …
Thread Warp 3
Thread Warp 8
Thread Warp 7
Thread Warp
Scalar
Thread
W
Scalar
Thread
X
Scalar
Thread
Y
Scalar
Thread
Z
Common PC
SIMD Pipeline
Notes: In SIMD, you need to specify the data array + an instruction (on which to operate the data on) + THE INSTRUCTION WIDTH. Eg: You might want to add 2 integer arrays of length 16, then a SIMD instruction would look like (the instruction has been cooked-up by me for demo) add.16 arr1 arr2 However, SIMT doesn't bother about the instruction width. So, essentially, you could write the above example as: arr1[i] + arr2[i] and then launch as many threads as the length of the array, as you want. Note that, if the array size was, let us say, 32, then SIMD EXPECTS you to explicitly call two such 'add.16' instructions! Whereas, this is not the case with SIMT.

## Slide 3: Loop Iterations as Threads
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Time
Slide credit: Krste Asanovic

## Slide 4: Memory Data Indexing
SIMT-execution model
Use thread id and block id to index data
Let’s assume N=16, blockDim=4  4 blocks
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
blockIdx.x = 0
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 0,1,2,3
blockIdx.x = 1
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 4,5,6,7
+
blockIdx.x = 2
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 8,9,10,11
blockIdx.x = 3
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 12,13,14,15
+
+
+
+

## Slide 5: Sample GPU SIMT Code (Simplified)
for (ii = 0; ii < 128; ++ii) {
C[ii] = A[ii] + B[ii];
}
// there are 128 threads
__global__ void KernelFunction(…) {
int tid = blockDim.x * blockIdx.x + threadIdx.x;
int varA = aa[tid];
int varB = bb[tid];
C[tid] = varA + varB;
}
CPU code
CUDA code
Slide credit: Hyesoon Kim

## Slide 6: Overview of GPU (Tesla) Architecture
Streaming
Multiprocessor
Streaming
Multiprocessor
Streaming
Multiprocessor
Interconnection Network
Global Memory (Device memory)
PC
I-Cache
Decoder
Shared Memory
Stream Processor
Stream Processor
Stream Processor
Stream Processor
Caches

## Slide 7: Execution Unit: Warp
T
T
T
T
T
T
T
T
SP
SP
SP
SP
SIMD Execution Unit
T
T
T
T
Warp is the basic unit of execution
  A group of threads (e.g. 32 threads for the Tesla GPU architecture)
Warp Execution
One warp
Sources ready
One warp
One warp
Inst 1
Inst 2
Inst 3
Sources ready
Sources ready
T
T
T
T
T
T
T
T
Finite number of streaming processors

## Slide 8: Register Read & ILP & TLP
Register read is fully pipelined.
Back-to-back operation is in the critical path
ILP across warps (~= TLP) can hide the latency of back-to-back
R1= R2+R3
R4= R1+R4
R1= R2+R3
R4= R1+R4
R1= R2+R3
R4= R1+R4
R1= R2+R3
R4= R1+R4
R1= R2+R3
R4= R1+R4
R1= R2+R3
R4= R1+R4
R1= R2+R3
R4= R1+R4
1 warp
24 cycles delay between 2 insts
1 warp
24 cycle delay is hidden by TLP
w0
wN
w1

## Slide 9: Latency Hiding with “Thread Warps”
Warp: A set of threads that execute the same instruction (on different data elements)
Fine-grained multithreading
  One instruction per thread in pipeline at a time (No branch prediction)
  Interleave warp execution to hide latencies
Register values of all threads stay in register file
No OS context switching
Memory latency hiding
  Graphics has millions of pixels
Decode
R
F
R
F
R
F
A
L
U
A
L
U
A
L
U
D-Cache
Thread Warp 6
Thread Warp 1
Thread Warp 2
Data
All Hit?
Miss?
Warps accessing
memory hierarchy
Thread Warp 3
Thread Warp 8
Writeback
Warps available
for scheduling
Thread Warp 7
I-Fetch
SIMD Pipeline
Slide credit: Tor Aamodt
Notes: With a large number of shader threads multiplexed on the same execution re- sources, our architecture employs fine-grained multithreading where individual threads are interleaved by the fetch unit to proactively hide the potential latency of stalls before they occur. As illustrated by Figure, warps are issued fairly in a round-robin queue. When a thread is blocked by a memory request, shader core simply removes that thread’s warp from the pool of “ready” warps and thereby allows other threads to proceed while the memory system processes its request.
With a large number of threads (1024 per shader core) interleaved on the same pipeline, FGMT effectively hides the latency of most memory operations since the pipeline is occupied with instructions from other threads while memory operations complete. also hides the pipeline latency so that data bypassing logic can potentially be omitted to save area with minimal impact on performance. simplify the dependency check logic design by restricting each thread to have at most one instruction running in the pipeline at any time.

## Slide 10: SPMD
Single procedure/program, multiple data
  This is a programming model rather than computer organization
Each processing element executes the same procedure, except on different data elements
  Procedures can synchronize at certain points in program, e.g. barriers
Essentially, multiple instruction streams execute the same program
  Each program/procedure can 1) execute a different control-flow path, 2) work on different data, at run-time
  Many scientific applications programmed this way and run on MIMD computers (multiprocessors)
  Modern GPUs programmed in a similar way on a SIMD computer

## Slide 11: Branch Divergence Problem in Warp-based SIMD
SPMD Execution on SIMD Hardware
  NVIDIA calls this “Single Instruction, Multiple Thread” (“SIMT”) execution
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B
C
D
E
F
A
G
Slide credit: Tor Aamodt

## Slide 12: Control Flow Problem in GPUs/SIMD
GPU uses SIMD pipeline to save area on control logic.
  Group scalar threads into warps
Branch divergence occurs when threads inside warps branch to different execution paths.
Branch
Path A
Path B
Branch
Path A
Path B
Slide credit: Tor Aamodt

## Slide 13: Branch Divergence Handling (I)
-
G
1111
TOS
B
C
D
E
F
A
G
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B/1111
C/1001
D/0110
E/1111
A/1111
G/1111
-
A
1111
TOS
E
D
0110
E
C
1001
TOS
-
E
1111
E
D
0110
TOS
-
E
1111
A
D
G
A
Time
C
B
E
-
B
1111
TOS
-
E
1111
TOS
Reconv. PC
Next PC
Active Mask
Stack
E
D
0110
E
E
1001
TOS
-
E
1111
Slide credit: Tor Aamodt

## Slide 14: What About Memory Divergence?
Modern GPUs have caches
Ideally: Want all threads in the warp to hit (without conflicting with each other)
Problem: One thread in a warp can stall the entire warp if it misses in the cache.
Need techniques to
  Tolerate memory divergence
  Integrate solutions to branch and memory divergence

## Slide 15: NVIDIA GeForce GTX 285
NVIDIA-speak:
  240 stream processors
  “SIMT execution”
Generic speak:
  30 cores
  8 SIMD functional units per core
Slide credit: Kayvon Fatahalian

## Slide 16: NVIDIA GeForce GTX 285 “core”
…
= instruction stream decode
= SIMD functional unit, control
shared across 8 units
= execution context storage
= multiply-add
= multiply
64 KB of storage
for fragment contexts (registers)
Slide credit: Kayvon Fatahalian
Notes: 30 * 32 * 32 = 30 * 1024 = 30K fragments
64KB register file = 16 32-bit registers per thread = 64B (1/32 that of LRB)
16KB of shared scratch
80KB / core available to software

## Slide 17: NVIDIA GeForce GTX 285 “core”
…
64 KB of storage
for thread contexts (registers)
Groups of 32 threads share instruction stream (each group is a Warp)
Up to 32 warps are simultaneously interleaved
Up to 1024 thread contexts can be stored
Slide credit: Kayvon Fatahalian
Notes: To get maximal latency hiding:
Run 1/32 of the time
16 words per thread = 64B

## Slide 18: NVIDIA GeForce GTX 285
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
There are 30 of these things on the GTX 285: 30,720 threads
Slide credit: Kayvon Fatahalian
Notes: If you’re running a CUDA program, and your not launching 30K threads, you are certainly not getting full latency hiding, and you might not be using the GPU well