## Slide 1: ECE4100/ECE6100/CS420/CS6290
Thanks to Prof. Kim for slides

## Slide 2: What to do with branches?
-Eliminate branches
  Predication (more on later)
Delayed branch slot
  SPARC, MIPS
Dual-path execution (more on later)
Or predict? 

## Slide 3: Control Dependencies
Branches are very frequent
  Approx. 20% of all instructions
Can not wait until we know where it goes
  Long pipelines
    Branch outcome is known after B cycles
    No scheduling past the branch until outcome known
  Superscalars (e.g., 4-way)
    Branch every cycle or so!
    One cycle of work, then bubbles for ~B cycles?

## Slide 4: Surviving Branches: Prediction
Predict Branches
  And predict them well!
Fetch, decode, etc. on the predicted path
  Option 1: No execution until branch is resolved
  Option 2: Execute anyway (speculation)
Recover from mispredictions
  Restart fetch from correct path

## Slide 5: Branch Prediction
Need to know two things
  Whether the branch is taken or not (direction)
  The target address if it is taken (target)
Direct jumps, Function calls: unconditional branches
  Direction known (always taken), target easy to compute
Conditional Branches (typically PC-relative)
  Direction difficult to predict, target easy to compute
Indirect jumps, function returns
  Direction known (always taken), target difficult

## Slide 6: Branch Prediction: Direction
Needed for conditional branches
  Most branches are of this type
Many, many kinds of predictors for this
  Static: fixed rule, or compiler annotation (e.g. br.bwh (branch whether hint. IA-64))
  Dynamic: hardware prediction
Dynamic prediction usually history-based
  Example: predict direction is the same as the last time this branch was executed

## Slide 7: Static Prediction
Always predict NT
  easy to implement
  30-40% accuracy … not so good
Always predict T
  60-70% accuracy
BTFNT
  loops usually have a few iterations, so this is like always predicting that the loop is taken
  don’t know target until decode

## Slide 8: One-Bit Branch Predictor: Last-time predictor
K bits of branch instruction address
Index
Branch history table of 2^K entries, 1 bit per entry
Use this entry to predict this branch:
0: predict not taken
1: predict taken
When branch direction resolved, go back into the table and update entry: 0 if not taken, 1 if taken

## Slide 9: One-Bit Branch Predictor (cont’d)
0xDC08: for(i=0; i < 100000; i++)
{
0xDC44: if( ( i % 100) == 0 )
        CountHundred( );
0xDC50: if( (i & 1) == 1)
CountOddNums( );
        }
T
N
T

## Slide 10: The Bit Is Not Enough!
Example: short loop (8 iterations)
  Taken 7 times, then not taken once
  Not-taken mispredicted (was taken previously)
  Act: TTTTTTTNTTTTTTNTTTTTTTNT…
  Pred: XTTTTTTTNTTTTTTNTTTTTTTN
  Corr: Xooooo MMooooooMMooooooMM
  Misprediction rate: 2/8 = 25%
Execute the same loop again
  First always mispredicted (previous outcome was not taken)
  Then 6 predicted correctly
  Then last one mispredicted again
Each fluke/anomaly in a stable pattern results in two mispredicts per loop

## Slide 11: Examples
DC08: TTTTTTTTTTT ... TTTTTTTTTTNTTTTTTTTT …
100,000 iterations
How often is branch outcome != previous outcome?
2 / 100,000
TN
NT
DC44: TTTTT ... TNTTTTT … TNTTTTT …
2 / 100
DC50: TNTNTNTNTNTNTNTNTNTNTNTNTNTNT …
2 / 2
99.998%
Prediction
Rate
98.0%
0.0%

## Slide 12: Two Bits are Better Than One
0
1
FSM for Last-time
Prediction
0
1
2
3
FSM for 2bC
(2-bit Counter)
Predict NT
Predict T
Transistion on T outcome
Transistion on NT outcome

## Slide 13: Example
2
T

3
T
3
T


…
3
N

N
1

T
0

0
T
1
T
T
T
T
…
T
1
1
1
1






T
1

T
…
1

0
T
1
T
2
T
3
T
3
T
…
3
T






Initial Training/Warm-up
1bC:
2bC:
Only 1 Mispredict per N branches now!
DC08: 99.999% DC44: 99.0%
0
1
2
3

## Slide 14: Importance of Branches
98%  99%
  Who cares?
  Actually, it’s 2% misprediction rate  1%
  That’s a halving of the number of mispredictions
So what?
  If a pipeline can fetch 5 instructions at a cycle and the branch resolution time is 20 cycles
  To Fetch 500 instructions
  100 accuracy : 100 cycles
  98 accuracy:
    100 (correctly fetch) + 20 (misprediction)*10 = 300 cycles
  99 accuracy
    100 (correctly fetch) + 20 misprediction *5 = 200 cycles

## Slide 15: Two-level Branch Predictor
1 1 ….. 1 0
BHR
(branch history register)
00 …. 00
00 …. 01
00 …. 10
11 …. 11
0
1
2
3
index
Pattern History Table
previous one
Yeh&patt’92

## Slide 16: BHR (Branch History Register)
0 0 0 0 0 0
History length
Initialization value (0 or 1)
1 : branch is taken
0: branch is not-taken
Old history
New history
New BHR = old BHR<<1 | (br_dir)
Example
BHR: 00000
Br1 : taken  BHR 00001
Br 2: not-taken  BHR 00010
Br 3: taken  BHR 00101

## Slide 17: Why does Global Predictor Work?
Branches are correlated
Branch X: if (cond1)
….
Branch Y: if (cond 2)
….
Branch Z : if (cond 1 and cond 2)
…….1 0
Branch X | Branch Y | Branch Z
1 | 0 | 0
1 | 1 | 1
0 | 1 | 0
0 | 0 | 0
BHR
…….1 1
…….01
…….00
PHT

## Slide 18: Gshare Branch Predictor
1 1 ….. 1 0
2bc
2bc
2bc
2bc
BHR
index
0x809000
PC
XOR
McFarling’93
Predictor size: 2^(history length)*2bit

## Slide 19: Exercise
There are three static branches, br1, br2, br3. dynamic branch trace is T,N,T,T,T,T,N,N,T (br1,br2, br3 is repeated three times). 3 bit BHR (start from 000).
PC addresses of the branches are 1,2,3 respectively.

## Slide 20: Agree Predictor
Most branches are biased
Interference in PHT entries
  Constructive (T+T, or N+N)
  Destructive (T+N, or N+T)
  Agree predictor  Check if branches agree with Bias direction (most entries will agree)
  Reduces destructive interference in PHT

## Slide 21: Global vs. Local Branch History
Local Behavior
  What is the predicted direction of Branch A given the outcomes of previous instances of Branch A?
Global Behavior
  What is the predicted direction of Branch Z given the outcomes of all* previous branches A, B, …, X and Y?
  * number of previous branches tracked limited by the history length

## Slide 22: Tournament Predictors (Hybrid predictor)
No predictor is clearly the best
  Different branches exhibit different behaviors
    Some “constant”, some global, some local
Idea: Let’s have a predictor to predict which predictor will predict better 

## Slide 23: Tournament Hybrid Predictors
Pred0
Pred1
Meta-
Predictor
Final Prediction
table of 2-/3-bit counters
Pred0 | Pred1 | Meta Update
 |  | ---
 |  | Inc
 |  | Dec
 |  | ---
If meta-counter MSB = 0,
use pred0 else use pred1

## Slide 24: Common Combinations
Global history + Local history
“easy” branches + global history
  2bC and gshare
short history + long history
Many types of behaviors, many combinations

## Slide 25: Perceptron Predictor
Use machine learning to train a branch predictor
Outcome is not always taken or not-taken
Train weight factors
Requires much smaller storage
Negative: complex calculation (solution: pipelining), linearly inseperable (solution: piece-wise linear predictor)

## Slide 26: Branch-Predicting Perceptron
Inputs (x’s) are from branch history and are -1 or +1
n + 1 small integer weights (w’s) learned by on-line training
Output (y) is dot product of x’s and w’s; predict taken if y ≥ 0
Training finds correlations between history and outcome
from D. Jimenez’s slides

## Slide 27: Training Algorithm
from D. Jimenez’s slides

## Slide 28: What Do The Weights Mean?
The bias weight, w0:
  Proportional to the probability that the branch is taken
  Doesn’t take into account other branches; just like a Smith predictor
The correlating weights, w1 through wn:
  wi is proportional to the probability that the predicted branch agrees with the ith branch in the history
The dot product of the w’s and x’s
  wi × xi is proportional to the probability that the predicted branch is taken based on the correlation between this branch and the ith branch
  Sum takes into account all estimated probabilities
What’s θ?
  Keeps from overtraining; adapt quickly to changing behavior
from D. Jimenez’s slides

## Slide 29: Organization of the Perceptron Predictor
Keeps a table of m perceptron weights vectors
Table is indexed by branch address modulo m
[Jiménez & Lin, HPCA 2001]
from D. Jimenez’s slides

## Slide 30: Seznec’s Predictors: OGEHL
The basis (inspired by earlier work on multiple tables and combining)
L(0)
?
L(4)
L(3)
L(2)
L(1)
TO
T1
T2
T3
T4

## Slide 31: GEometric History Length predictor
The set of history lengths forms a geometric series
What is important: L(i)-L(i-1) is drastically increasing
most of the storage
for short history !!
{0, 2, 4, 8, 16, 32, 64, 128}
Capture correlation
on very long histories

## Slide 32: TAGE: Geometric history length + partial tags + optimized update policy
pc
h[0:L1]
ctr
u
tag
hash
hash
=?
ctr
u
tag
hash
hash
=?
ctr
u
tag
hash
hash
=?
prediction
pc
pc
h[0:L2]
pc
h[0:L3]
1
1
1
1
1
1
1
1
1
Tagless base
predictor

## Slide 33: TAGE
Considered the state-of-the-art in branch prediction
Winner of Championship Branch Prediction (2006, 2011, 2014)
Some variant of TAGE likely to be in modern processors
For more detailed working, check out these papers:
A. Seznec, Pierre Michaud “A Case for (partially) tagged Geometric History Length Branch Prediction”, JILP 2006
A. Seznec, “A 256Kbits L-TAGE Predictor” in CBP-2, 2006

## Slide 34: Target Address Prediction
Branch Target Buffer
  IF stage: need to know fetch addr every cycle
  Need target address one cycle after fetching a branch
  For some branches (e.g., indirect) target known only after EX stage, which is way too late
  Even easily-computed branch targets need to wait until instruction decoded and direction predicted in ID stage (still at least one cycle too late)
  So, we have a fast predictor for the target that only needs the address of the branch instruction

## Slide 35: Branch Target Buffer
BTB indexed by instruction address (or fetch address)
We don’t even know if it is a branch!
If address matches a BTB entry, it is predicted to be a branch
BTB entry tells whether it is taken (direction) and where it goes if taken
BTB takes only the instruction address, so while we fetch one instruction in the IF stage we are predicting where to fetch the next one from
Direction prediction can be factored out into separate table

## Slide 36: Branch Target Buffer

## Slide 37: Prediction at Fetch Stage with BTB
target address
Direction predictor (2-bit counters, etc.)
Cache of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
PC + inst size
taken?
Next Fetch
Address
hit?
Address of the
current branch

## Slide 38: Function Calls
main()
{
  foo();
  printf(“still hungry\n”);
  ….
  foo();
  printf(“full\n”);
}
foo(){
…..
  return
  }
BTB
??

## Slide 39: Return Address Stack (RAS)
Function returns are frequent, yet
  Address is difficult to compute (have to wait until EX stage done to know it)
  Address difficult to predict with BTB (function can be called from multiple places)

## Slide 40: Function Calls
main()
{
  foo();
  printf(“still hungry\n”);
  ….
  foo();
  printf(“full\n”);
}
foo(){
…..
  return
  }
0x800
0x804
0x900
0x904

## Slide 41: Return Address Stack (RAS)
But return address is actually easy to predict
  It is the address after the last call instruction that we haven’t returned from yet
  Hence the Return Address Stack

## Slide 42: Function Calls
main()
{
  foo();
  printf(“still hungry\n”);
  ….
  foo();
  printf(“full\n”);
}
foo(){
…..
  return
  }
0x800
0x804
0x900
0x904
0x904
0x804

## Slide 43: Return Address Stack (RAS)
Call pushes return address into the RAS
When a return instruction decoded, pop the predicted return address from RAS
Accurate prediction even w/ small RAS

## Slide 44: LOOP Branches
Special treatment for loop branches
for (ii =0; ii < 10; ii++)
{
…
}
Loop branch is iterated 10 times all the time

## Slide 45: Options
Prepare to branch (HPL-PD)
  Software gives hints to the hardware about what the branch target will be. It saves us the target prediction since it has already been written into one of the target registers.
Special Loop predictor (Intel’s Pentium M)
  Detect a loop branch
  Train the max iteration counter value

## Slide 46: Pentium-M (cont’d)
Local component also has support for loops
  accurately predict branches of the form (TkN)*

## Slide 47: Direct vs. Indirect Branch
TARG
A+1
A
T
N
a
b
A
d
?
Conditional (Direct) Branch
Indirect Branch
r
br.cond TARGET
R1 = MEM[R2]
branch R1
Use the BTB
A special indirect branch predictor (Intel’s Core-2)

## Slide 48: Indirect Branch Predictors
Tagged Target Cache (Chang‘97)
History Information
Branch Address
Hash Function
Target Cache
Target address

## Slide 49: Avoiding Branch Prediction
Predicated Execution
Dual-path execution
  When you see a low-confidence branch, start to fetch from only two paths
  See another low-confidence branch?
    Ignore and just keep only two paths
Multi-path execution
  Whenever it sees a low-confidence branch, forks

## Slide 50: Predication (Predicated Execution)
D
D
Idea: Compiler converts control dependency into a data dependency  branch is eliminated
  Each instruction has a predicate bit set based on the predicate computation
  Only instructions with TRUE predicates are committed (others turned into NOPs)
(normal branch code)
C
B
D
A
T
N
p1 = (cond)
branch p1, TARGET
mov b, 1
jmp JOIN
TARGET:
mov b, 0
A
B
C
B
C
D
A
(predicated code)
A
B
C
if (cond) {
b = 0;
}
else {
b = 1;
}
p1 = (cond)
(!p1) mov b, 1
(p1) mov b, 0
add x, b, 1
add x, b, 1

## Slide 51: Predicated Execution (II)
Predicated execution can be high performance and energy-efficient
Fetch Decode Rename Schedule RegisterRead Execute
A
B
C
D
A
E
F
Predicated Execution
Branch Prediction
Pipeline flush!!
E
D
B
F
nop
Fetch Decode Rename Schedule RegisterRead Execute
A
B
A
C
B
A
C
B
D
A
D
C
B
E
A
E
D
C
F
B
A
F
E
D
C
B
A
A
F
B
C
D
E
F
E
D
A
B
C
F
E
A
B
C
D
F
E
D
C
B
A
F
E
D
C
A
B
E
D
C
B
A
F
A
F
B
C
D
E

## Slide 52: Predicated Execution (III)
Advantages:
  + Eliminates mispredictions for hard-to-predict branches
  + No need for branch prediction for some branches
  + Good if misprediction cost > useless work due to predication
  + Enables code optimizations hindered by the control dependency
  + Can move instructions more freely within predicated code
Disadvantages:
  -- Causes useless work for branches that are easy to predict
  -- Reduces performance if misprediction cost < useless work
  -- Adaptivity: Static predication is not adaptive to run-time branch behavior. Branch behavior changes based on input set, phase, control-flow path.
  -- Additional hardware and ISA support
  -- Cannot eliminate all hard to predict branches
  -- Loop branches?

## Slide 53: Conditional Move Operations
Very limited form of predicated execution
CMOV R1  R2
  R1 = (ConditionCode == true) ? R2 : R1
  Employed in most modern ISAs (x86, Alpha)

## Slide 54: Dual-path Execution
Low-confidence
C
D
E
F
B
D
E
F
A
B
C
D
E
F
path 1
path 2
Dual-path
G
Low-confidence

## Slide 55: Multi-path Execution
Low-confidence
C
D
E
F
B
D
E
F
A
B
C
D
E
F
path 1
path 2
Multi-path
G
Low-confidence
G
path 3
G
path 4
I
H
I
H
I
H

## Slide 56: High-Bandwidth Fetch: Collapsing Buffer
Fetch from two cache blocks, rotate, collapse past taken branches
Thomas M. Conte, Kishore N. Menezes, Patrick M. Mills and Burzin A. Patel. Optimization of Instruction Fetch Mechanisms for High Issue Rates. International Symposium on Computer Architecture, June 1995.

## Slide 57: High-Bandwidth Fetch: Trace Cache
Fold out taken branches by tracing instructions as they commit into a fill buffer
Eric Rotenberg, S. Bennett, and James E. Smith. Trace Cache: A Low Latency Approach to High Bandwidth Instruction Fetching. MICRO, December 1996.

## Slide 58: Intel Pentium 4 Trace Cache
No first-level instruction cache: trace cache only
Trace cache BTB identifies next trace
Miss leads to fetch from level two cache
Trace cache instructions are decoded (uops)
Cache capacity 12k uops
  Overwhelmed for database applications
  Serial decoder becomes performance bottleneck