## Slide 1: ECE4100/ECE6100/CS4290/CS6290
Thanks to Prof. Kim, Prof. Loh & Prof. Prvulovic

## Slide 2: Amdahl’s Law
If we help only a limited portion of the execution time, then the portion we do not help starts to dominate
Parallel (P)
Serial
P/2
Serial
Serial
P/4
Serial
P/8
Serial
P/infinity
Max Speedup =
1
(S+P/N)

## Slide 3: Multiprocessing
Flynn’s Taxonomy of Parallel Machines
  How many Instruction streams?
  How many Data streams?
SISD: Single I Stream, Single D Stream
  A uniprocessor
SIMD: Single I, Multiple D Streams
  Each “processor” works on its own data
  But all execute the same instrs in lockstep
  E.g. a vector processor or MMX, CUDA

## Slide 4: Flynn’s Taxonomy
MISD: Multiple I, Single D Stream
  Not used much
  Stream processors are closest to MISD
MIMD: Multiple I, Multiple D Streams
  Each processor executes its own instructions and operates on its own data
  This is your typical off-the-shelf multiprocessor (made using a bunch of “normal” processors)
  Includes multi-core processors

## Slide 5: Flynn’s Classical Taxonomy
SISD Single Instruction, Singe Data | SIMD Single Instruction, Multiple Data
MISD Multiple Instruction, Single Data | MIMD Multiple Instruction, Multiple Data
Notes: In the SIMD model there are two types of architectures:
1. Shared-memory model; and
2. Direct-connection networks

## Slide 6: Multiprocessors
ILP limits
reached?
Why do we need multiprocessors?
  Uniprocessor speed keeps improving
  But there are things that need even more speed
    Wait for a few years for Moore’s law to catch up?
    Or use multiple processors and do it now?
Multiprocessor software problem
  Most code is sequential (for uniprocessors)
    MUCH easier to write and debug
  Correct parallel code very, very difficult to write
    Efficient and correct is even harder
    Debugging even more difficult (Heisenbugs)

## Slide 7: MIMD Multiprocessors
Centralized Shared Memory
Distributed Memory

## Slide 8: Centralized-Memory Machines
Also “Symmetric Multiprocessors” (SMP)
“Uniform Memory Access” (UMA)
  All memory locations have similar latencies
  Data sharing through memory reads/writes
  P1 can write data to a physical address A, P2 can then read physical address A to get that data
Problem: Memory Contention
  All processor share the one memory
  Memory bandwidth becomes bottleneck
  Used only for smaller machines
    Most often 2,4, or 8 processors

## Slide 9: Distributed-Memory Machines
Two kinds
  Distributed Shared-Memory (DSM)
    All processors can address all memory locations
    Data sharing like in SMP
    Also called NUMA (non-uniform memory access)
    Latencies of different memory locations can differ (local access faster than remote access)
  Message-Passing
    A processor can directly address only local memory
    To communicate with other processors, must explicitly send/receive messages
    Also called multicomputers or clusters
Most accesses local, so less memory contention (can scale to well over 1000 processors)

## Slide 10: Message-Passing Machines
A cluster of computers
  Each with its own processor and memory
  An interconnect to pass messages between them
  Producer-Consumer Scenario:
    P1 produces data D, uses a SEND to send it to P2
    The network routes the message to P2
    P2 then calls a RECEIVE to get the message
  Two types of send primitives
    Synchronous: P1 stops until P2 confirms receipt of message
    Asynchronous: P1 sends its message and continues
  Standard libraries for message passing: Most common is MPI – Message Passing Interface

## Slide 11: Message Passing Example
1
10
20
5
6
8
11
25
14
25
50
Master
Slave
Slave

## Slide 12: Message Passing: A Program
Calculating the sum of array elements
#define ASIZE 1024
#define NUMPROC 4
double myArray[ASIZE/NUMPROC];
double mySum=0;
for(int i=0;i<ASIZE/NUMPROC;i++)
mySum+=myArray[i];
if(myPID=0){
for(int p=1;p<NUMPROC;p++){
int pSum;
recv(p,pSum);
mySum+=pSum;
}
printf(“Sum: %lf\n”,mySum);
}else
send(0,mySum);
Must manually split the array
“Master” processor adds up partial sums and prints the result
“Slave” processors send their partial results to master

## Slide 13: Message Passing Pros and Cons
Pros
  Simpler and cheaper hardware
  Explicit communication makes programmers aware of costly (communication) operations
Cons
  Explicit communication is painful to program
  Requires manual optimization
    If you want a variable to be local and accessible via LD/ST, you must declare it as such
    If other processes need to read or write this variable, you must explicitly code the needed sends and receives to do this

## Slide 14: Communication Performance
Metrics for Communication Performance
  Communication Bandwidth
  Communication Latency
    Sender overhead + transfer time + receiver overhead
  Communication latency hiding
Characterizing Applications
  Communication to Computation Ratio
    Work done vs. bytes sent over network
    Example: 146 bytes per 1000 instructions

## Slide 15: Shared Memory Example
11
14
1
10
20
5
6
8
39
50
25

## Slide 16: Shared Memory: A Program
Calculating the sum of array elements
#define ASIZE 1024
#define NUMPROC 4
shared double array[ASIZE];
shared double allSum=0;
shared mutex sumLock;
double mySum=0;
for(int i=myPID*ASIZE/NUMPROC;i<(myPID+1)*ASIZE/NUMPROC;i++)
mySum+=array[i];
lock(sumLock);
allSum+=mySum;
unlock(sumLock);
if(myPID=0)
printf(“Sum: %lf\n”,allSum);
Array is shared
Each processor adds its partial sums to the final result
“Master” processor prints the result
Each processor sums up “its” part of the array

## Slide 17: Shared Memory Pros and Cons
Pros
  Communication happens automatically
  More natural way of programming
    Easier to write correct programs and gradually optimize them
  No need to manually distribute data (but can help if you do)
Cons
  Needs more hardware support
  Easy to write correct, but inefficient programs (remote accesses look the same as local ones)

## Slide 18: PopQuiz
Deep Blue vs. Kasparov (1997)
Small dataset, lots of parallelism
Shared memory or message passing?

## Slide 19: Multi Processors

## Slide 20: Implementing MP Machines
One approach: add sockets to your MOBO
  minimal changes to existing CPUs
  power delivery, heat removal and I/O not too bad since each chip has own set of pins and cooling
CPU0
CPU1
CPU2
CPU3
Pictures found from google images

## Slide 21: Chip-Multiprocessing
Simple SMP on the same chip
Intel “Smithfield” Block Diagram
AMD Dual-Core Athlon FX
Pictures found from google images

## Slide 22: Shared Caches
Resources can be shared between CPUs
  ex. IBM Power 5
CPU0
CPU1
L2 cache shared between
both CPUs (no need to
keep two copies coherent)
L3 cache is also shared (only tags
are on-chip; data are off-chip)

## Slide 23: 6-core world!

## Slide 24: Benefits?
Cheaper than mobo-based SMP
  all/most interface logic integrated on to main chip (fewer total chips, single CPU socket, single interface to main memory)
  less power than mobo-based SMP as well (communication on-die is more power-efficient than chip-to-chip communication)
Performance
  on-chip communication is faster
Efficiency
  potentially better use of hardware resources than trying to make wider/more OOO single-threaded CPU

## Slide 25: Performance vs. Power
2x CPUs not necessarily equal to 2x performance
2x CPUs  ½ power for each
  maybe a little better than ½ if resources can be shared
Back-of-the-Envelope calculation:
  3.8 GHz CPU at 100W
  Dual-core: 50W per CPU
  P  V3: Vorig3/VCMP3 = 100W/50W  VCMP = 0.8 Vorig
  f  V: fCMP = 3.0GHz
Benefit of SMP: Full power
budget per socket!

## Slide 26: Performance vs. Power (2)
So what’s better?
  One 3.8 GHz CPU?
  Or a dual-core running at 3.0 GHz?
Depends on workloads
  If you have one program to run, the 3.8GHz CPU will run it in 79% of the time
  If you have two programs to run, then:
    3.8GHz CPU: 79% for one, or 158% for both
    Dual 3.0GHz CPU: 100% for both in parallel

## Slide 27: Question
Dual Core: total power 200W frequency: 2GHz
With the same power budget if we have 4 cores, what should be the frequency of each core?
Assume that the power is equally distributed
  P  V3:
  Vdual3/Vquad3 = 100W/50W  Vquad = 0.8 Vdual
  f  V: fquad = 1.6GHz