## Slide 1: Precise Exceptions and Out-of-Order
Moinuddin K. Qureshi

## Slide 2: Multi-Cycle Execution
Not all instructions take the same amount of time for “execution”
Idea: Have multiple different functional units that take different number of cycles
  Can be pipelined or not pipelined
  Can let independent instructions to start execution on a different functional unit before a previous long-latency instruction finishes execution

## Slide 3: Issues in Pipelining: Multi-Cycle Execute
Instructions can take different number of cycles in EXECUTE stage
  Integer ADD versus FP MULtiply
  What is wrong with this picture?
    What if FMUL incurs an exception?
    Sequential semantics of the ISA NOT preserved!
F
D
E
W
F
D
E
W
E
E
E
E
E
E
E
FMUL R4  R1, R2
ADD R3  R1, R2
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
FMUL R2  R5, R6
ADD R4  R5, R6
F
D
E
W
E
E
E
E
E
E
E

## Slide 4: Exceptions vs. Interrupts
Exceptions versus interrupts
Cause
  Exceptions: internal to the running thread
  Interrupts: external to the running thread
When to Handle
  Exceptions: when detected (and known to be non-speculative)
  Interrupts: when convenient
    Except for very high priority ones
      Power failure
      Machine check
Priority: process (exception), depends (interrupt)
Handling Context: process (exception), system (interrupt)

## Slide 5: Precise Exceptions/Interrupts
The architectural state should be consistent when the exception/interrupt is ready to be handled
1. All previous instructions should be completely retired.
2. No later instruction should be retired.
Retire = commit = finish execution and update arch. state

## Slide 6: Why Do We Want Precise Exceptions?
Semantics of the von Neumann model ISA specifies it
  Remember von Neumann vs. dataflow
Aids software debugging
Enables (easy) recovery from exceptions, e.g. page faults
Enables (easily) restartable processes
Enables traps into software (e.g., software implemented opcodes)

## Slide 7: Ensuring Precise Exceptions in Pipelining
Idea: Make each operation take the same amount of time
Downside
  What about memory operations?
  Each functional unit takes 500 cycles?
F
D
E
W
F
D
E
W
E
E
E
E
E
E
E
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
FMUL R3  R1, R2
ADD R4  R1, R2

## Slide 8: Solutions
Reorder buffer
History buffer
Future register file
Checkpointing
Recommended Reading
  Smith and Plezskun, “Implementing Precise Interrupts in Pipelined Processors” IEEE Trans on Computers 1988 and ISCA 1985.
  Hwu and Patt, “Checkpoint Repair for Out-of-order Execution Machines,” ISCA 1987.
We will discuss this in detail

## Slide 9: Reorder Buffer (ROB)
Idea: Complete instructions out-of-order, but reorder them before making results visible to architectural state
When instruction is decoded it reserves an entry in the ROB
When instruction completes, it writes result into ROB entry
When instruction oldest in ROB and it has completed without exceptions, its result moved to reg. file or memory
Register
File
Func Unit
Func Unit
Func Unit
Reorder
Buffer
Instruction
Cache

## Slide 10: Reorder Buffer: Independent Operations
Results first written to ROB, then to register file at commit time
What if a later operation needs a value in the reorder buffer?
  Read reorder buffer in parallel with the register file. How?
F
D
E
W
F
D
E
R
E
E
E
E
E
E
E
F
D
E
W
F
D
E
R
F
D
E
R
F
D
E
R
F
D
E
R
E
E
E
E
E
E
E
W
R
R
W
W
W
W

## Slide 11: Reorder Buffer: How to Access?
A register value can be in the register file, reorder buffer, (or bypass paths)
Register
File
Func Unit
Func Unit
Func Unit
Reorder
Buffer
Instruction
Cache
bypass path
Content
Addressable
Memory
(searched with
register ID)

## Slide 12: Simplifying Reorder Buffer Access
Idea: Use indirection
Access register file first
  If register not valid, register file stores the ID of the reorder buffer entry that contains (or will contain) the value of the register
  Mapping of the register to a ROB entry
Access reorder buffer next
What is in a reorder buffer entry?
V
DestRegID
DestRegVal
StoreAddr
StoreData
PC/IP
Control/valid bits
Exc?

## Slide 13: What is Wrong with This Picture?
What is R4’s value at the end?
  The first FMUL’s result
  Output dependency not respected
F
D
E
W
F
D
E
W
E
E
E
E
E
E
E
FMUL R4  R1, R2
ADD R3  R1, R2
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
FMUL R2  R5, R6
ADD R4  R5, R6
F
D
E
W
E
E
E
E
E
E
E

## Slide 14: Register Renaming with a Reorder Buffer
Output and anti dependencies are not true dependencies
  WHY? The same register refers to values that have nothing to do with each other
  They exist due to lack of register ID’s (i.e. names) in the ISA
The register ID is renamed to the reorder buffer entry that will hold the register’s value
  Register ID  ROB entry ID
  Architectural register ID  Physical register ID
  After renaming, ROB entry ID used to refer to the register
This eliminates anti- and output- dependencies
  Gives the illusion that there are a large number of registers

## Slide 15: In-Order Pipeline with Reorder Buffer
Decode (D): Access regfile/ROB, allocate entry in ROB, check if instruction can execute, if so dispatch instruction
Execute (E): Instructions can complete out-of-order
Completion (R): Write result to reorder buffer
Retirement/Commit (W): Check for exceptions; if none, write result to architectural register file or memory; else, flush pipeline and start from exception handler
In-order dispatch/execution, out-of-order completion, in-order retirement
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store
R

## Slide 16: Reorder Buffer Pros and Cons
Pro
  Conceptually simple for supporting precise exceptions
  Can eliminate false dependencies
Con
  Reorder buffer needs to be accessed to get the results that are yet to be written to the register file
    CAM or indirection  increased latency and complexity

## Slide 17: Checking for and Handling Exceptions in Pipelining
When the oldest instruction ready-to-be-retired is detected to have caused an exception, the control logic
  Recovers architectural state (register file, IP, and memory)
  Flushes all younger instructions in the pipeline
  Saves IP and registers (as specified by the ISA)
  Redirects the fetch engine to the exception handling routine

## Slide 18: Out-of-Order Execution (Dynamic Instruction Scheduling)

## Slide 19: Review: In-order pipeline
Problem: A true data dependency stalls dispatch of younger instructions into functional (execution) units
Dispatch: Act of sending an instruction to a functional unit
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Cache miss

## Slide 20: Can We Do Better?
What do the following two pieces of code have in common (with respect to execution in the previous design)?
Answer: First ADD stalls the whole pipeline!
  ADD cannot dispatch because its source registers unavailable
  Later independent instructions cannot get executed
How are the above code portions different?
  Answer: Load latency is variable (unknown until runtime)
  What does this affect? Think compiler vs. microarchitecture
IMUL R3  R1, R2
ADD R3  R3, R1
ADD R1  R6, R7
IMUL R5  R6, R8
ADD R7  R3, R5
LD R3  R1 (0)
ADD R3  R3, R1
ADD R1  R6, R7
IMUL R5  R6, R8
ADD R7  R3, R5

## Slide 21: Out-of-order Execution (Dynamic Scheduling)
Idea: Move the dependent instructions out of the way of independent ones
  Rest areas for dependent instructions: Reservation stations
Monitor the source “values” of each instruction in the resting area
When all source “values” of an instruction are available, “fire” (i.e. dispatch) the instruction
  Instructions dispatched in dataflow (not control-flow) order
Benefit:
  Latency tolerance: Allows independent instructions to execute and complete in the presence of a long latency operation

## Slide 22: In-order vs. Out-of-order Dispatch
In order dispatch:
Tomasulo + precise exceptions:
16 vs. 12 cycles
F
D
W
E
E
E
E
R
F
D
E
R
W
F
IMUL R3  R1, R2
ADD R3  R3, R1
ADD R1  R6, R7
IMUL R5  R6, R8
ADD R7  R3, R5
D
E
R
W
F
D
E
R
W
F
D
E
R
W
F
D
W
E
E
E
E
R
F
D
STALL
STALL
E
R
W
F
D
E
E
E
E
STALL
E
R
F
D
E
E
E
E
R
W
F
D
E
R
W
WAIT
WAIT
W

## Slide 23: Enabling OoO Execution
1. Need to link the consumer of a value to the producer
  Register renaming: Associate a “tag” with each data value
2. Need to buffer instructions until they are ready
  Insert instruction into reservation stations after renaming
3. Instructions need to keep track of readiness of source values
  Broadcast the “tag” when the value is produced
  Instructions compare their “source tags” to the broadcast tag  if match, source value becomes ready
4. When all source values of an instruction are ready, dispatch the instruction to functional unit (FU)
  What if more instructions become ready than available FUs?

## Slide 24: Tomasulo’s Algorithm
OoO with register renaming invented by Robert Tomasulo
  Used in IBM 360/91 Floating Point Units
  Read: Tomasulo, “An Efficient Algorithm for Exploiting Multiple Arithmetic Units,” IBM Journal of R&D, Jan. 1967.
What is the major difference today?
  Precise exceptions: IBM 360/91 did NOT have this
  Patt, Hwu, Shebanow, “HPS, a new microarchitecture: rationale and introduction,” MICRO 1985.
  Patt et al., “Critical issues regarding HPS, a high performance microarchitecture,” MICRO 1985.
Variants used in most high-performance processors
  Most notably Pentium Pro, Pentium M, Intel Core(2), AMD K series,
  Alpha 21264, MIPS R10000, IBM POWER5, Oracle UltraSPARC T4

## Slide 25: Two Humps in a Modern Pipeline
Hump 1: Reservation stations (scheduling window)
Hump 2: Reordering (reorder buffer, aka instruction window or active window)
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store
R
E
O
R
D
E
R
S
C
H
E
D
U
L
E
TAG and VALUE Broadcast Bus
in order
out of order
in order

## Slide 26: Register Renaming
Output and anti dependencies are not true dependencies
  WHY? The same register refers to values that have nothing to do with each other
  They exist because not enough register ID’s (i.e. names) in the ISA
The register ID is renamed to the reservation station entry that will hold the register’s value
  Register ID  RS entry ID
  Architectural register ID  Physical register ID
  After renaming, RS entry ID used to refer to the register
This eliminates anti- and output- dependencies
  Approximates the performance effect of a large number of registers even though ISA has a small number

## Slide 27: An Exercise
Assume ADD (4 cycle execute), MUL (6 cycle execute)
Assume one adder and one multiplier
How many cycles
  in a non-pipelined machine
  in an in-order-dispatch pipelined machine with imprecise exceptions (no forwarding and full forwarding)
  in an out-of-order dispatch pipelined machine imprecise exceptions (full forwarding)
MUL R3  R1, R2
ADD R5  R3, R4
ADD R7  R2, R6
ADD R10  R8, R9
MUL R11  R7, R10
ADD R5  R5, R11
F
D
E
W

## Slide 28: An Exercise, with Precise Exceptions
Assume ADD (4 cycle execute), MUL (6 cycle execute)
Assume one adder and one multiplier
How many cycles
  in a non-pipelined machine
  in an in-order-dispatch pipelined machine with reorder buffer (no forwarding and full forwarding)
  in an out-of-order dispatch pipelined machine with reorder buffer (full forwarding)
MUL R3  R1, R2
ADD R5  R3, R4
ADD R7  R2, R6
ADD R10  R8, R9
MUL R11  R7, R10
ADD R5  R5, R11
F
D
E
R
W