## Slide 1: Pipeline Basics
Moinuddin K Qureshi

## Slide 2: How to Design a Fast Processor?
Perform Execution Quickly
Get Instructions
Quickly
Get Data
Quickly

## Slide 3: Pipelining
Fundamental for faster processing
Key idea:
Instruction processing involves many steps. Eg. Fetch, Decode..
Don’t wait for processing of next instructions till all steps finish
Need: Latches to store intermediate state
Decode
Fetch
Execute
Memory
Write
back

## Slide 4: Latches
Latch: holds value for the next cycle.
We assume edge latch.
The latch value is changed at the end of clock cycle.
Input set up & hold
010101
1
1
Combinational logic
latch
Combinational logic

## Slide 5
Basic Five Stage Pipeline
Fetch
Dec
Exec
Mem
WB
Reg
File

## Slide 6: Each Stage can take Multiple Cycles
Example: MIPS R4000
IF
ID
MEM
WB
integer unit
FP/int Multiply
FP adder
FP/int divider
ex
m1
m2
m3
m4
m5
m6
m7
a1
a2
a3
a4
Div (lat = 25, Init inv=25)

## Slide 7: Pipelining: Dependencies
Two types of Dependencies: Control and Data
Control Dependency: Which instruction to fetch?
Data Dependency:
Read after write (RAW dependency) – TRUE dependency
Write after Read (WAR dependency) – Can be avoided
Write after Write (WAW dependency) – Can be avoided
How about “Read after Read” ??

## Slide 8: Data Dependence Types
Flow dependence
      r3  r1 op r2 Read-after-Write
      r5  r3 op r4 (RAW)
Anti dependence
      r3  r1 op r2 Write-after-Read
      r1  r4 op r5 (WAR)
Output-dependence
      r3  r1 op r2 Write-after-Write
      r5  r3 op r4 (WAW)
      r3  r6 op r7

## Slide 9: Interlocking
Detection of dependence between instructions in a pipelined processor to guarantee correct execution
Software based interlocking
vs.
Hardware based interlocking
Quiz: “MIPS” acronym?

## Slide 10: Approaches to Dependence Detection
Scoreboarding
  Each register in register file has a Valid bit associated with it
  An instruction that is writing to the register resets the Valid bit
  An instruction in Decode stage checks if all its source and destination registers are Valid
    Yes: No need to stall… No dependence
    No: Stall the instruction
Advantage:
  Simple. 1 bit per register
Disadvantage:
  Need to stall for all types of dependences, not only RAW dep

## Slide 11: Approaches to Dependence Detection
Combinational dependence check logic
  Special logic that checks if any instruction in later stages is supposed to write to any source register of the instruction that is being decoded
  Yes: stall the instruction/pipeline
  No: no need to stall… no RAW dependence
Advantage:
  No need to stall on WAR and WAW dependences
Disadvantage:
  Logic is more complex than a scoreboard
  Logic becomes more complex as we make the pipeline deeper and wider (superscalar)

## Slide 12: No Data Dependencies
Cycle Num | FETCH | DECODE | EXECUTE | MEMORY | WBACK
1 | A |  |  |  | 
2 | B | A |  |  | 
3 | C | B | A |  | 
4 | D | C | B | A | 
5 | E | D | C | B | A
6 | F | E | D | C | B
7 | G | F | E | D | C
8 | H | G | F | E | D
Assume a program where all instructions (A-H) are independent

## Slide 13: Data Dependencies
Cycle Num | FETCH | DECODE | EXECUTE | MEMORY | WBACK
1 | A |  |  |  | 
2 | B | A |  |  | 
3 | C | B (R2?) | A |  | 
4 | C | B (R2?) |  | A | 
5 | C | B (R2?) |  |  | A(R2,end)
6 | C | B (R2) |  |  | 
7 |  | C | B |  | 
8 |  |  | C | B | 
9 |  |  |  | C | B
A: ADD R2, R1, R0
B: ADD R3, R2, R0
C: ADD R7, R5, R4
Fetch
Dec
Exec
Mem
WB
Reg
File

## Slide 14: Forwarding (nominal)
Cycle Num | FETCH | DECODE | EXECUTE | MEMORY | WBACK
1 | A |  |  |  | 
2 | B | A |  |  | 
3 | C | B (R2?) | A |  | 
4 | C | B (R2?) |  | A | 
5 | C | B (R2) |  |  | A(R2OK)
6 |  |  | B |  | 
7 |  |  | C | B | 
8 |  |  |  | C | B
9 |  |  |  |  | C
A: ADD R2, R1, R0
B: ADD R3, R2, R0
C: ADD R7, R5, R4
Fetch
Dec
Exec
Mem
WB
Reg
File
MUX

## Slide 15: Quiz on Forwarding

## Slide 16: Forwarding (all stages)
A: ADD R2, R1, R0
B: ADD R3, R2, R0
C: ADD R7, R5, R4
Fetch
Dec
Exec
Mem
WB
Reg
File
MUX

## Slide 17: Forwarding (all stages)
Cycle Num | FETCH | DECODE | EXECUTE | MEMORY | WBACK
1 | A |  |  |  | 
2 | B | A |  |  | 
3 | C | B (R2) | A(Bypass) |  | 
4 |  | C | B | A | 
5 |  |  | C | B | A
6 |  |  |  | C | B
7 |  |  |  |  | C
8 |  |  |  |  | 
9 |  |  |  |  | 
A: ADD R2, R1, R0
B: ADD R3, R2, R0
C: ADD R7, R5, R4

## Slide 18: Super-Scalar Pipelines
Cycle Num | FETCH | DECODE | EXECUTE | MEMORY | WBACK
1 | A,B |  |  |  | 
2 | C,D | A,B |  |  | 
3 | E,F | C,D | A,B |  | 
4 | G,H | E,F | C,D | A,B | 
5 | I,J | G,H | E,F | C,D | A,B
6 | K,L | I,J | G,H | E,F | C,D
7 | M,N | K,L | I,J | G,H | E,F
F1
F2
D1
E1
M1
W1
D2
E2
M2
W2
2 in
2 out?
Assume independent instructions A-N
How about the complexity of Dependency Check and Forwarding?

## Slide 19: What about Control Dependency?
Cycle Num | FETCH | DECODE | EXECUTE | MEMORY | WBACK
1 | A |  |  |  | 
2 | B (stall) | A |  |  | 
3 | B (stall) |  | A |  | 
4 | B (stall) |  |  | A (PC OK) | 
5 | C |  |  |  | A
6 |  | C |  |  | 
7 |  |  | C |  | 
8 |  |  |  | C | 
9 |  |  |  |  | C
A: BR nzp, C
B: ADD R3,R3, #5
C: ADD R7, R5, R4
Fetch
Dec
Exec
Mem
WB
PC

## Slide 20: Why is this an important bottleneck?
On average, 20% of the instructions are control flow (branches)
Lets assume a machine with CPI=1
For 20% of instructions, we have to add three cycles of bubbles.
What is the net CPI?
Let there be 100 instructions, so perfect cycles=100
20 instructions @ 3 extra cycles = 60 cycles additional
Total cycles = 100+60 = 160  Net CPI is now 1.6
Slowdown of 60% !
Modern pipelines are 15-20 deep, so 12-16 bubbles per branch!
What can we do to mitigate this problem?

## Slide 21: Architecture Timing Simulation
Timing simulation
Simulate how many cycles to execute programs
In the previous example, how many cycles?
   Finding out how many cycles? That’s the timing simulator

## Slide 22: Trace driven vs. Execution driven
Trace driven: instructions are all executed
  Easy to develop a simulator
  Could be faster to simulate
  Our lab assignment
Execution driven: simulator executes instructions during simulation time.
  Development time is longer.
  Can simulate wrong-path instructions, multi thread instruction behavior