## Slide 1: ECE 4100/6100 CS6290/4290 Advanced Computer Architecture Prefetching
Prof. Moinuddin Qureshi Georgia Institute of Technology
Thanks to Prof. Mutlu (CMU) for slides

## Slide 2: Prefetching
If memory takes a long time, start accessing earlier
Load
L1
L2
Data
DRAM
Total Load-to-Use Latency
Prefetch
Data
Load
Much improved Load-to-Use Latency
Somewhat improved Latency
May cause resource
contention due to
extra cache/DRAM
activity

## Slide 3: Prefetching
Fetch the data before it is needed (i.e. pre-fetch) by the program
Why?
  Memory latency is high. If we can prefetch accurately and early enough we can reduce/eliminate that latency.
  Can eliminate compulsory cache misses
  Can eliminate all cache misses? Capacity, conflict, coherence?
Predicts which address will be needed in the future
  Works if programs have predictable miss address patterns
  Note: In modern systems, prefetching is usually done in cache block granularity

## Slide 4: Prefetching: The Four Questions
What
  What addresses to prefetch
When
  When to initiate a prefetch request
Where
  Where to place the prefetched data
How
  Software, hardware, execution-based, cooperative

## Slide 5: Challenges in Prefetching: What
What addresses to prefetch
  Prefetching useless data wastes resources
    Memory bandwidth
    Cache or prefetch buffer space
    Energy consumption
    These could all be utilized by demand requests or more accurate prefetch requests
  Accurate prediction of addresses to prefetch is important
    Prefetch accuracy = used prefetches / sent prefetches
How do we know what to prefetch
  Predict based on past access patterns
  Use the compiler’s knowledge of data structures
Prefetching algorithm determines what to prefetch

## Slide 6: Challenges in Prefetching: When
When to initiate a prefetch request
  Prefetching too early
    Prefetched data might not be used before it is evicted from storage
  Prefetching too late
    Might not hide the whole memory latency
When a data item is prefetched affects the timeliness of the prefetcher
Prefetcher can be made more timely by
  Making it more aggressive: try to stay far ahead of the processor’s access stream (hardware)
  Moving the prefetch instructions earlier in the code (software)

## Slide 7: Challenges in Prefetching: Where
Where to place the prefetched data
  In cache
    + Simple design, no need for separate buffers
    -- Can evict useful demand data  cache pollution
  In a separate prefetch buffer
    + Demand data protected from prefetches  no cache pollution
    -- More complex memory system design
    - Where to place the prefetch buffer
    - When to access the prefetch buffer (parallel vs. serial with cache)
    - When to move the data from the prefetch buffer to cache
    - How to size the prefetch buffer
    - Keeping the prefetch buffer coherent
Many modern systems place prefetched data into the cache
  Intel Pentium 4, Core2’s, AMD systems, IBM POWER4,5,6, …

## Slide 8: Challenges in Prefetching: How
Software prefetching
  ISA provides prefetch instructions
  Programmer or compiler inserts prefetch instructions (effort)
  Usually works well only for “regular access patterns”
Hardware prefetching
  Hardware monitors processor accesses
  Memorizes or finds patterns/strides
  Generates prefetch addresses automatically
Execution-based prefetchers
  A “thread” is executed to prefetch data for the main program
  Can be generated by either software/programmer or hardware

## Slide 9: Software Prefetching (I)
Idea: Compiler/programmer places prefetch instructions into appropriate places in code
  Mowry et al., “Design and Evaluation of a Compiler Algorithm for Prefetching,” ASPLOS 1992.
Two types: binding vs. non-binding
  Binding: Prefetch into a register (using a regular load)
    + No need for a separate “prefetch” instruction
    -- Takes up registers. Exceptions?
    -- What if another processor modifies the data value before it is used?
  Non-binding: Prefetch into cache (special instruction?)
    + No coherence issues since caches are coherent
    -- Prefetches treated differently from regular loads

## Slide 10: Software Prefetching (II)
Can work for very regular array-based access patterns. Issues:
  -- Prefetch instructions take up processing/execution bandwidth
  How early to prefetch? Determining this is difficult
    -- Prefetch distance depends on hardware implementation (memory latency, cache size, time between loop iterations)  portability?
    -- Going too far back in code reduces accuracy (branches in between)
  Need “special” prefetch instructions in ISA?
    Not really. Alpha load into register 31 treated as prefetch (r31==0)
    PowerPC dcbt (data cache block touch) instruction
  -- Not easy to do for pointer-based data structures
for (i=0; i<N; i++) {
__prefetch(a[i+8]);
__prefetch(b[i+8]);
sum += a[i]*b[i];
}
while (p) {
__prefetch(pnext);
work(pdata);
p = pnext;
}

## Slide 11: Hardware Prefetching (I)
Idea: Specialized hardware observes load/store access patterns and prefetches data based on past access behavior
Tradeoffs:
  + Can be tuned to system implementation
  + No code portability issues (in terms of performance variation between implementations)
  + Does not waste instruction execution bandwidth
  -- More hardware complexity to detect patterns
  - Software can be more efficient in some cases

## Slide 12: Next-Line Prefetchers
Simplest form of hardware prefetching: always prefetch next N cache lines after a demand access (or a demand miss)
  Next-line prefetcher (or next sequential prefetcher)
  Tradeoffs:
    + Simple to implement. No need for sophisticated pattern detection
    + Works well for sequential/streaming access patterns (instructions?)
    -- Can waste bandwidth with irregular patterns
    - What is the prefetch accuracy if access stride = 2 and N = 1?
    -- What if the program is traversing memory from higher to lower addresses?
    - Also prefetch “previous” N cache lines?

## Slide 13: Stride Prefetchers
Two kinds
  Instruction program counter (PC) based
  Cache block address based
Instruction based:
  Baer and Chen, “An effective on-chip preloading scheme to reduce data access penalty,” SC 1991.
  Idea:
    Record the distance between the memory addresses referenced by a load instruction (i.e. stride of the load) as well as the last address referenced by the load
    Next time the same load instruction is fetched, prefetch last address + stride

## Slide 14: Instruction Based Stride Prefetching
What is the problem with this?
  Hint: how far can this get ahead? How much of the miss latency can the prefetch cover?
  Initiating the prefetch when the load is fetched the next time can be too late
    Load will access the data cache soon after it is fetched!
  Solutions:
    Use lookahead PC to index the prefetcher table
    Prefetch ahead (last address + N*stride)
    Generate multiple prefetches
Load Inst. | Last Address | Last | Confidence
PC (tag) | Referenced | Stride | 
……. | ……. | …… | 
Load
Inst
PC

## Slide 15: Cache-Block Address Based Stride Prefetching
Can detect
  A, A+N, A+2N, A+3N, …
  Stream buffers are a special case of cache block address based stride prefetching where N = 1
Address tag | Stride | Control/Confidence
……. | …… | 
Block
address

## Slide 16: Prefetcher Performance (I)
Accuracy (used prefetches / sent prefetches)
Coverage (prefetched misses / all misses)
Timeliness (on-time prefetches / used prefetches)
Bandwidth consumption
  Memory bandwidth consumed with prefetcher / without prefetcher
  Good news: Can utilize idle bus bandwidth (if available)
Cache pollution
  Extra demand misses due to prefetch placement in cache
  More difficult to quantify but affects performance

## Slide 17: Prefetcher Performance (II)
Prefetcher aggressiveness affects all performance metrics
Aggressiveness dependent on prefetcher type
For most hardware prefetchers:
  Prefetch distance: how far ahead of the demand stream
  Prefetch degree: how many prefetches per demand access
Predicted Stream
Predicted Stream
X
Access Stream
Pmax
Prefetch Distance
Pmax
Very Conservative
Pmax
Middle of the Road
Pmax
Very Aggressive
P
Prefetch Degree
X+1
1 2 3

## Slide 18: Prefetcher Performance (III)
How do these metrics interact?
Very Aggressive
  Well ahead of the load access stream
  Hides memory access latency better
  More speculative
  + Higher coverage, better timeliness
  -- Likely lower accuracy, higher bandwidth and pollution
Very Conservative
  Closer to the load access stream
  Might not hide memory access latency completely
  Reduces potential for cache pollution and bandwidth contention
  + Likely higher accuracy, lower bandwidth, less polluting
  -- Likely lower coverage and less timely

## Slide 19: Prefetcher Performance (IV)
  Srinath et al., “Feedback Directed Prefetching: Improving the Performance and Bandwidth-Efficiency of Hardware Prefetchers“, HPCA 2007.
48%
 29%

## Slide 20: How to Cover More Irregular Access Patterns?
More irregular access patterns
  Indirect array accesses
  Linked data structures
  Multiple regular strides (1,2,3,1,2,3,1,2,3,…)
  Random patterns?
  Generalized prefetcher for all patterns?
Correlation based prefetchers
Content-directed prefetchers
Precomputation or execution-based prefetchers

## Slide 21: Markov Prefetching (I)
Consider the following history of cache block addresses
  A, B, C, D, C, E, A, C, F, F, E, A, A, B, C, D, E, A, B, C, D, C
After referencing a particular address (say A or E), are some addresses more likely to be referenced next
A
B
C
D
E
F
1.0
.33
.5
.2
1.0
.6
.2
.67
.6
.5
.2
Markov
Model

## Slide 22: Markov Prefetching (II)
Track the likely next addresses after seeing a particular address
Prefetch accuracy is generally low so prefetch up to N next addresses to increase coverage
Prefetch accuracy can be improved by using longer history
  Decide which address to prefetch next by looking at the last K load addresses instead of just the current one
  e.g., index with the XOR of the data addresses from the last K loads
  Using history of a few loads can increase accuracy dramatically
Joseph and Grunwald, “Prefetching using Markov Predictors,” ISCA 1997.
Cache Block Addr |  | Prefetch | Confidence | …. | Prefetch | Confidence
(tag) |  | Candidate 1 |  | …. | Candidate N | 
……. |  | ……. | …… | .… | ……. | ……
 |  |  |  | …. |  | 
Cache
Block
Addr

## Slide 23: Content Directed Prefetching (I)
A specialized prefetcher for pointer values
Cooksey et al., “A stateless, content-directed data prefetching mechanism,” ASPLOS 2002.
Idea: Identify pointers among all values in a fetched cache block and issue prefetch requests for them.
+ No need to memorize/record past addresses!
+ Can eliminate compulsory misses (never-seen pointers)
-- Indiscriminately prefetches all pointers in a cache block
How to identify pointer addresses:
  Compare address sized values within cache block with cache block’s address  if most-significant few bits match, pointer

## Slide 24: Content Directed Prefetching (II)
x40373551
L2
DRAM
…
…
=
=
=
=
=
=
=
=
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
x80011100
Generate Prefetch
Virtual Address Predictor
X80022220
22220
X800
11100
x800

## Slide 25: Hybrid Hardware Prefetchers
Many different access patterns
  Streaming, striding
  Linked data structures
  Localized random
Idea: Use multiple prefetchers to cover all patterns
+ Better prefetch coverage
-- More complexity
-- More bandwidth-intensive
-- Prefetchers start getting in each other’s way
Global History Buffer: natural structure for hybrid prefetchers

## Slide 26: Execution-based Prefetchers
Idea: Pre-execute a piece of the (pruned) program solely for prefetching data
  Only need to distill pieces that lead to cache misses
  Speculative thread: Pre-executed program piece can be considered a “thread”
  Speculative thread can be executed
    On a separate processor/core
    On a separate hardware thread context (think fine-grained multithreading)
    On the same thread context in idle cycles (during cache misses)

## Slide 27: Thread-Based Pre-Execution
Dubois and Song, “Assisted Execution,” USC Tech Report 1998.
Chappell et al., “Simultaneous Subordinate Microthreading (SSMT),” ISCA 1999.
Zilles and Sohi, “Execution-based Prediction Using Speculative Slices”, ISCA 2001.

## Slide 28: Thread-Based Pre-Execution Issues
Where to execute the precomputation thread?
  1. Separate core (least contention with main thread)
  2. Separate thread context on the same core (more contention)
  3. Same core, same context
    When the main thread is stalled
When to spawn the precomputation thread?
  1. Insert spawn instructions well before the “problem” load
    How far ahead?
      Too early: prefetch might not be needed
      Too late: prefetch might not be timely
  2. When the main thread is stalled
When to terminate the precomputation thread?
  1. With pre-inserted CANCEL instructions
  2. Based on effectiveness/contention feedback

## Slide 29: Runahead Execution
A simple pre-execution method for prefetching purposes
When the oldest instruction is a long-latency cache miss:
  Checkpoint architectural state and enter runahead mode
In runahead mode:
  Speculatively pre-execute instructions
  The purpose of pre-execution is to generate prefetches
  L2-miss dependent instructions are marked INV and dropped
Runahead mode ends when the original miss returns
  Checkpoint is restored and normal execution resumes
Mutlu et al., “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors,” HPCA 2003.

## Slide 30: Runahead Execution (Mutlu et al., HPCA 2003)
Compute
Compute
Load 1 Miss
Miss 1
Stall
Compute
Load 2 Miss
Miss 2
Stall
Load 1 Miss
Runahead
Load 2 Miss
Load 2 Hit
Miss 1
Miss 2
Compute
Load 1 Hit
Saved Cycles
Small Window:
Runahead:

## Slide 31: Runahead Execution (III)
Advantages:
  + Very accurate prefetches for data/instructions (all cache levels)
  + Follows the program path
  + No need to construct a pre-execution thread
  + Uses the same thread context as main thread, no waste of context
  + Simple to implement, most of the hardware is already built in
Disadvantages/Limitations:
  -- Extra executed instructions
  -- Limited by branch prediction accuracy
  -- Cannot prefetch dependent cache misses. Solution?
  -- Effectiveness limited by available MLP
  -- Prefetch distance limited by memory latency
Implemented in IBM POWER6, Sun “Rock”