## Slide 1: CS4290/CS6290/ECE4100/ECE6100
Thanks to Prof. Kim, Prof. Prvulovic and Prof. Loh

## Slide 2: In order vs. OOO
fetch
decode
issue
exec
write
commit
fetch
decode
issue
exec
write
commit
In-order
Out of order
In-order

## Slide 3: Re-Order Buffer (ROB)
Separates architected vs. physical registers
Tracks program order of all in-flight insts
  Enables in-order completion or “commit”

## Slide 4: Hardware Organization
Instruction Buffers
op
Qj
Qk
Vj
Vk
Reservation Stations and ALUs
op
Qj
Qk
Vj
Vk
op
Qj
Qk
Vj
Vk
op
Qj
Qk
Vj
Vk
Add
op
Qj
Qk
Vj
Vk
op
Qj
Qk
Vj
Vk
Mult
Architected Register File
RAT
type
dest
value
fin
ROB
“head”

## Slide 5: Issue
Read inst from inst buffer
Check if resources available:
  Appropriate RS entry
  ROB entry
Read RAT, read (available) sources, update RAT
Write to RS and ROB
Instruction Buffers
op
Qj
Qk
Vj
Vk
Reservation Stations and ALUs
op
Qj
Qk
Vj
Vk
op
Qj
Qk
Vj
Vk
op
Qj
Qk
Vj
Vk
Add
op
Qj
Qk
Vj
Vk
op
Qj
Qk
Vj
Vk
Mult
Architected Register File
RAT
type
dest
value
fin
ROB
“head”
Stall issue if any needed resource not available

## Slide 6: Exec
Same as before
  Wait for all operands to arrive
  Compete to use functional unit
  Execute!

## Slide 7: Write Result
Broadcast result on Common Data Bus
  (any dependents will grab the value)
Write result back to your ROB entry
  The ARF holds the “official” register state, which we will only update in program order
  Mark ready/finished bit in ROB (note that this inst has completed execution)
Reservation station can be freed.

## Slide 8: New: Commit
When an inst is the oldest in the ROB
  i.e., ROB-head points to it
Write result (if ready/finished bit is set)
  If register producing instruction: write to architected register file
  If store: write to memory
    Q: What about load?
Advance ROB-head to next instruction
This is what the outside world sees
  And it’s all in-order

## Slide 9: Commit Illustrated
Make instruction execution “visible” to the outside world
  “Commit” the changes to the architected state
A
B
C
D
E
F
G
H
J
K










ARF
WB result
Outside World “sees”:
A executed
B executed
C executed
D executed
E executed
ROB
Instructions execute out of program order,
but outside world still “believes” it’s in-order

## Slide 10: Revisiting Register Renaming
R1
R2+R3
ROB
ROB1
ROB2
ROB3
ROB4
ROB5
ROB6
ROB7
ROB8
R1 = R2 + R3
R3 = R5 – R6
R1 = R1 * R7
R1 = R4 + R8
R2 = R9 + R3
R1
R2
R3
R1
R2
R3
RAT
…
ROB1
R3
R5-R6
ROB2
R1
ROB1*R7
ROB3
R1
R4+R8
If we issue R2=R9+R3 to the
ROB now, R3 comes from ROB2
Then update RAT so when we issue R2=R9+R3, it will read source from the ARF.
ROB4
R2
R9+ROB2
However, if R3=R5-R6 commits first…
R2
R9+R3

## Slide 11: Unified Reservation Stations (1)
If MULT RS’s are full, and we need to issue another MULT, then we have to stall
  But there may be other RS’s (e.g., add) that are available
  Proper number of RS’s per ALU needs to be matched to the program’s inst distribution
    But different programs have different distributions

## Slide 12: Unified Reservation Stations (2)
RS (Adder)
RS (Mul/Div)
Add
Mult
Add
Mult
RS (Unified)
Can hold 5 adds
Or 5 multiplies
Or any combination

## Slide 13: Unified Reservation Stations (3)
Arbitration and execution paths a little more complex (not too bad though)
ADD rdy
MUL x
ADD x
ADD rdy
MUL rdy
MUL x
ADD x
ADD rdy
RS Entries
Adder Arbiter
Multiplier Arbiter
Ready add’s compete for execution unit
Ready mul’s do the same
Arbitration logic picks insts to execute
Add
Mult
Insts go and do their thing
For N functional units, RS needs
To support N read ports

## Slide 14: Out-of-Order, but not Superscalar
As described, this Tomasulo (+ROB) CPU can only maintain sustained throughput of 1 IPC
Limitations:
  Need superscalar fetch, decode, etc.
  There’s only one CDB, so only one inst per cycle can write-back its result to the ROB
  Also must commit > 1 IPC

## Slide 15: Getting > 1 IPC
Must be able to issue > 1 IPC to RS/ROB
Must be able to send > 1 IPC to functional units
  original Tomasulo can do this already (if inst ready and FU available, go and execute!)
Must be able to write-back > 1 IPC to ROB (and reservation stations)

## Slide 16: Dual-Issue
Need to check resource availability for two instructions (RS/ROB entries)
  Depending on resources, may issue 0,1 or 2
Read RAT/ARF/ROB for operands
  Renaming is a little trickier (next slide)
Update RS/ROB entries (not too hard)

## Slide 17: Dual-Rename
R1 = R2 + R3
R4 = R2 – R4
ARF1
ROB17
ARF3
ROB6
R1
R2
R3
R4
RAT
Read current mappings for all operands
New destinations are just in the next two ROB entries
To be allocated: ROB_tail, ROB_tail + 1
ROB21
ROB22
ROB17, ARF3
ROB17, ROB6
All registers renamed!
R1 = R2 + R3
R4 = R1 – R4
ARF1
ROB17
ARF3
ROB6
R1
R2
R3
R4
RAT
ROB21
ROB22
ROB17, ARF3
ARF1, ROB6
X
=?
dst1
=?
src2L
src2R
From
RAT
New
ROB
entry
From
RAT
New
ROB
entry
Need to check for RAW
dependencies within your
issue group

## Slide 18: Multiple CDB’s
It works (we do this today in CPUs)
But there’s a cost
  each RS entry must compare each source with each CDB
  more area, logic, power (all  $$$)
D1, ROB3
E1, ROB4
A2, ROB10
A1, ROB7
B1, ROB19
C1, ROB2
Arbiters
FU
FU
FU
FU
CDB1
RS Entries
CDB2
ROB7
ROB4

## Slide 19: Committing > 1 IPC
Must be able to write-back multiple results from ROB  ARF (or memory for stores)
  ROB needs extra read ports
  ARF needs extra write ports

## Slide 20: Terminology is Inconsistent, Overloaded
Issue, Dispatch, Commit, etc.
  Text uses terms w.r.t. Tomasulo’s algorithm
  Other usage is different (many academics)
  Issue/Alloc/Dispatch
  Exec/Issue/Dispatch
  Commit/Complete/Retire/Graduate
Blue: Intel’s convention
Orange: some academics

## Slide 21: Check Point Mechanism
R1 | PR12
R2 | PR13
R3 | PR14
R4 | PR15
fetch
decode
issue
exec
write
commit
Add r1, r2, r3
Br target
Sub r3,r5, r6
Mul r2, r5, #1
Br target 2
Add r5, r1,#-1
Sub R2, R2, R3
R1 | PR16
R2 | PR13
R3 | PR14
R4 | PR15
R1 | PR16
R2 | PR 17
R3 | PR18
R4 | PR15
ARF
PRF
RAT

## Slide 22: In order vs. OOO
fetch
decode
issue
exec
write
commit
fetch
decode
issue
exec
write
commit
In-order
Out of order
In-order