## Slide 1: ECE4100/ECE6100/CS4290/CS6290

## Slide 2: Comparing Speedup
Two machines: IPC_A Freq_A & IPC_B Freq_B
Speedup = OldTime/NewTime
Speedup_B = Time_with_A/Time_with_B
Exec Time inversely proportional to IPC & Freq
Speedup_B = (Freq_B*IPC_B) = Freq_B IPC_B
(Freq_A*IPC_A) Freq_A IPC_A
Speedup Equals Frequency Ratio times IPC Ratio

## Slide 3: CPI Analysis
Lets build a simple model based on
Cycles Per Instruction (CPI stack)
Perfect CPI
CPI due to ILP
CPI due to Branch Predictor
CPI due to Memory

## Slide 4: Perfect CPI and ILP limitations
Perfect CPI depends on Machine width
  N wide cannot give an IPC more than N
Perfect CPI is not obtainable
  ILP limitation (more divergence for high N)
  Branch misprediction (flush pipeline)
  Memory limitations (bubbles from cache miss)

## Slide 5: Perfect CPI and ILP limitations
Perfect CPI depends on Machine width
  N wide cannot give an IPC more than N
Perfect CPI is not obtainable
  ILP limitation (more divergence for high N)
  Branch misprediction (flush pipeline)
  Memory limitations (bubbles from cache miss)
  Many other (TLB miss, port contention etc.)

## Slide 6: ILP Exploitation
Difficult to find many independent instruction every cycle
Example: Lets say for an N-wide issue machine (N<= 5)
we lose 0.1*N of issue width from limited ILP
N | 1 | 2 | 3 | 4 | 5
Perfect IPC | 1 | 2 | 3 | 4 | 5
Efficiency | 0.9 | 0.8 | 0.7 | 0.6 | 0.5
ILP limited IPC | 0.9 | 1.6 | 2.1 | 2.4 | 2.5

## Slide 7: Lets Add Branches Now
Lets say Branch Prediction accuracy is 95% and a conditional branch happens once every 5 instructions
Thus, pipeline gets flushed once every 100 instructions
Penalty depends on pipeline length (say L)
To a first order, if we have pipeline width W and length L we will flush L*W instructions every 100 instructions

## Slide 8: Impact of Pipeline Length
Let L=10 and W=4, 1GHz. To execute 100 instructions:
- A perfect machine need 25 cycles (IPC=4)
- ILP limited (perfect BP+mem): 42 cycles (IPC=2.4)
Every 100 instructions nothing for 10 cycles (branch mispredict), so 100 instructions in 52 cycles  IPC=1.94
If L=25 @ 2GHz then mispredict penalty is 25 cycle 100 instructions take 42+25=67 cycles  IPC=100/67= 1.5
Speedup = Freq_Ratio * IPC_Ratio = 2*(1.5/1.94)= 1.55

## Slide 9: What is going on?
IPC=2.4
42
10
IPC=2.4
IPC=2.4
Time(cycles)
L=10
IPC=2.4
42
25
IPC=2.4
IPC=2.4
Time(cycles)
L=25
IPC=2.4
IPC=2.4
IPC=2.4
42ns
IPC=2.4
IPC=2.4
Time(nano sec)
L=10
1GHz
IPC=2.4
21ns
Time(nano sec)
L=25
2GHz
IPC=2.4
IPC=2.4
12.5ns
IPC=2.4
IPC=2.4
10ns

## Slide 10: Now Lets Add Imperfect Memory
Let every fourth instruction be a load, impact depends on
Cache Miss Rate (b) Miss Penalty [Perfect I-side]
Let, pipeline length=10 MissRate=8% Penalty=20 cycles
With perfect memory it takes 52 cycles
25 LD, 2 misses, add 40 cycles, so 92 cycles (IPC=1.09)
Let, pipeline length=25 MissRate=8% Penalty=40 cycles
With perfect memory it takes 67 cycles
25 LD, 2 misses, add 80 cycles, so 147 cycles (IPC=0.68)
Speedup = Freq_Ratio * IPC_Ratio = 2*(0.68/1.09)= 1.25x

## Slide 11: Simple Model
Shows that we need to improve branch prediction accuracy and reduce memory penalties for deeply pipeline machines
Otherwise the benefits of deep pipeline (higher frequency) gets offset by increasing CPI
How about Out-of-Order
- It improves ILP exploitation
- Memory Level Parallelism
Exercise: Assume efficiency loss from width is only 0.05N
And we send two load misses in flight, what is IPC/speedup?