## Slide 1: Vector and SIMD
Slides derived from Prof. Onur Mutlu (CMU)

## Slide 2: SIMD Processing
Single instruction operates on multiple data elements
  In time or in space
Multiple processing elements

## Slide 3: Vector Processors
A vector is a one-dimensional array of numbers
Many scientific/commercial programs use vectors
    for (i = 0; i<=49; i++)
    C[i] = (A[i] + B[i]) / 2
A vector processor is one whose instructions operate on vectors rather than scalar (single data) values
Basic requirements
  Need to load/store vectors  vector registers (contain vectors)
  Need to operate on vectors of different lengths  vector length register (VLEN)
  Elements of a vector might be stored apart from each other in memory  vector stride register (VSTR)
    Stride: distance between two elements of a vector

## Slide 4: Vector Processors (II)
A vector instruction performs an operation on each element in consecutive cycles
  Vector functional units are pipelined
  Each pipeline stage operates on a different data element
Vector instructions allow deeper pipelines
  No intra-vector dependencies  no hardware interlocking within a vector
  No control flow within a vector
  Known stride allows prefetching of vectors into cache/memory

## Slide 5: Vector Processor Advantages
+ No dependencies within a vector
  Pipelining, parallelization work well
  Can have very deep pipelines, no dependencies!
+ Each instruction generates a lot of work
  Reduces instruction fetch bandwidth
+ Highly regular memory access pattern
  Interleaving multiple banks for higher memory bandwidth
  Prefetching
+ No need to explicitly code loops
  Fewer branches in the instruction sequence

## Slide 6: Vector Registers
Each vector data register holds N M-bit values
Vector control registers: VLEN, VSTR, VMASK
Vector Mask Register (VMASK)
  Indicates which elements of vector to operate on
  Set by vector test instructions
    e.g., VMASK[i] = (Vk[i] == 0)
Maximum VLEN can be N
  Maximum number of elements stored in a vector register
V0,0
V0,1
V0,N-1
V1,0
V1,1
V1,N-1
M-bit wide
M-bit wide

## Slide 7: Vector Machine Organization (CRAY-1)
CRAY-1
Russell, “The CRAY-1 computer system,” CACM 1978.
Scalar and vector modes
8 64-element vector registers
64 bits per element
16 memory banks
8 64-bit scalar registers
8 24-bit address registers

## Slide 8: SIMD Operations in Modern ISAs

## Slide 9: Intel Pentium MMX Operations
Idea: One instruction operates on multiple data elements simultaneously
  Designed with multimedia (graphics) operations in mind
Peleg and Weiser, “MMX Technology
Extension to the Intel Architecture,”
IEEE Micro, 1996.
No VLEN register
Opcode determines data type:
8 8-bit bytes
4 16-bit words
2 32-bit doublewords
1 64-bit quadword
Stride always equal to 1.

## Slide 10: MMX Example: Image Overlaying (I)