## Slide 1: ECE4100/ECE6100
Thanks to Prof. Kim, Prof. Loh, Prof. Pruvulovic for earlier versions of the lecture notes!

## Slide 2: Main Memory in the System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 3: The Memory Chip/System Abstraction

## Slide 4: SRAM vs. DRAM
DRAM = Dynamic RAM
SRAM: 6T per bit
  built with normal high-speed CMOS technology
DRAM: 1T per bit
  built with special DRAM process optimized for density

## Slide 5: Hardware Structures
b
b
SRAM
wordline
b
DRAM
wordline
Bit lines

## Slide 6: DRAM Chip Organization
Row Decoder
Sense Amps
Column Decoder
Memory
Cell Array
Row Buffer
Row
Address
Column
Address
Data Bus
Bit lines
Word lines

## Slide 7: DRAM Chip Organization (2)
Differences with SRAM
    reads are destructive: contents are erased after reading
  Row buffer/DRAM Page
    Read lots of bits all at once, and then parcel them out based on different column addresses
    Read from the same row buffer from different locations order

## Slide 8: DRAM Read Operation
Row Decoder
Sense Amps
Column Decoder
Memory
Cell Array
Row Buffer
0x1FE
0x000
Data Bus
0x001
0x002
Accesses need not be sequential

## Slide 9: Need for Writeback of DRAM Page
Row Buffer
So after a read, the contents of the DRAM cell are gone
The values are stored in the row buffer
Write them back into the cells for the next read in the future
Sense Amps
DRAM cells

## Slide 10: Memory subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
Processor
“Channel”

## Slide 11: Page Mode DRAM
A DRAM bank is a 2D array of cells: rows x columns
A “DRAM row” is also called a “DRAM page”
“Sense amplifiers” also called “row buffer”
Each address is a <row,column> pair
Access to a “closed row”
  Activate command opens row (placed into row buffer)
  Read/write command reads/writes column in the row buffer
  Precharge command closes the row and prepares the bank for next access
Access to an “open row”
  No need for activate command

## Slide 12: DRAM Bank Operation
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 8)
Column address 8
(Row 0, Column 80)
Column address 80
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 13: Latency Components:
CPU → controller transfer time
Controller latency
  Queuing & scheduling delay at the controller
  Access converted to basic commands
Controller → DRAM transfer time
DRAM bank latency
  Simple tCAS is row is “open” OR
  tACT + tCAS if array precharged OR
  tACT + tCAS + tPRE (worst case)
DRAM → CPU transfer time (through controller) tBUS

## Slide 14: Open Page vs. Close Page Policies
Open Page: Keep the row opened until a conflict
  A row buffer hit will take only CAS delay: say 10 ns +tBUS
  A row buffer conflict will take PRE+ACT+CAS: say 30 ns+tBUS
Close Page: Close the row buffer after access
  A row buffer miss take ACT+ CAS: say 10+10 = 20ns +tBUS
Right policy depends on row buffer hit rate
  Server processors typically use close page policy

## Slide 15: Address Mapping (Single Channel)
Single-channel system with 8-byte memory bus
  2GB memory, 8 banks, 4KB Row buffer, 64K rows per bank
  64 byte cache blocks (so 6 bits for line in Row Buffer)
Row interleaving
  Consecutive rows of memory in consecutive banks
Cache block interleaving
    Consecutive cache block addresses in consecutive banks
    Accesses to consecutive cache blocks serviced in parallel
    How about random accesses? Strided accesses?
Which Line in Row (6 bits)
BankID (3 bits)
Which Row in Bank (16 bits)
Which Line in Row (6 bits)
Which Row in Bank (16 bits)
BankID (3 bits)