## Slide 1: Introduction to Quantum Computing Systems
Swamit Tannu
Notes: Zoom out
What is computing
Do you know
Error Correction?
Quantum computing

## Slide 2: Plan for todays lecture
Context
Limits to existing computing paradigm
What is Quantum Computing?
What can we engineers do?

## Slide 3: Computing is Transformation

## Slide 4: At the Beginning of Computer Engineering
Left: J. William Mauchly
Right: J. Presper Eckert
John Von-Neumann

## Slide 5: Von-Neumann Architecture

## Slide 6: Computing Stack
Problem
Algorithms
PL & Compilers
Architecture
Devices/Technology
Circuits
Electrons

## Slide 7: Iron Law for Performance
OS
Customers
Architect
Designer

## Slide 8: Architectural Innovations in last 30 years
Better functional units – Adders, multipliers, shifters, pipelined architectures
Front-end ideas – feed the daemon, i-cache, Branch Predictors, Trace-caches
Out of Order – Find more ILP, ROB, Wide issue machines
Reduce Memory Latency -- Data Caches, LD-ST Ques
From single thread to multi-thread – ILP to task-level parallelism, SMT, GPU

## Slide 9: Moore’s Law
Technology Scaling  2x transistors every ~2 years

## Slide 10: Limited Voltage Scaling

## Slide 11: Thermal Challenges

## Slide 13: Scaling Improves Memory and Compute Capacity
cell
cell
cell
cell
Technology Scaling
DRAM Chip
Courtesy: Prashant Nair

## Slide 14
DRAM Chip
Cell
Scaling Deteriorates Reliability
Courtesy: Prashant Nair

## Slide 15
DRAM Chip
Scaling Deteriorates Reliability
Courtesy: Prashant Nair

## Slide 16
DRAM Chip
✖
✖
✖
✖
Courtesy: Prashant Nair
Scaling Deteriorates Reliability
Notes: Redudancy and Error Correction

## Slide 17
Courtesy: Prashant Nair
Sparing faulty cells in DRAM
Notes: Redudancy and Error Correction

## Slide 18
Courtesy: Prashant Nair
Sparing faulty cells in DRAM
Notes: Redudancy and Error Correction

## Slide 19
Courtesy: Prashant Nair
Single Error Correct Double Error Detect (SECDED)
ECC Chip
Data Chips
Using Error Correction to fight faulty cells in DRAM
Notes: Redudancy and Error Correction

## Slide 20
Courtesy: Prashant Nair
Corrects single-bit fault in each word (8 Bytes)
For 8GB DIMM  1 Billion words
✖
ECC Chip
✖
20
Single Error Correct Double Error Detect (SECDED)
Using Error Correction to fight faulty cells in DRAM
Notes: Redudancy and Error Correction

## Slide 21: There is Path Towards 3nm Transistors

## Slide 23: General Purpose Vs Special Purpose

## Slide 24: Rise of Domain Specific Accelerators

## Slide 25: What’s Next?
Problem
Algorithms
PL & Compilers
Architecture
Devices/Technology
Circuits
Electrons

## Slide 26: Why Build Quantum Computers?
Can solve fundamentally hard problems
On existing computers, time to solve class of problems grow exponentially with problem size
Execution Time
Classical Computer
Problem Size
100+ Years
Prime Factorization
Notes: Quantum computers promise solutions to problems that are extremely hard to solve on a conventional computer.

## Slide 27: Potential of Quantum Computers
Factoring a 2048-bit number
100+ years & Consume all energy of earth
Quantum computer can factor 2048-bit number in about 27 hours
(Ref: A. G. Fowler: arxiv.org/abs/1208.0928)

## Slide 28: Potential of Quantum Computers
Factoring a 2048-bit number
100+ years
Consume all energy of earth
Quantum Computer
Shor’s factoring Algorithm
26.7 hours
A. G. Fowler: arxiv.org/abs/1208.0928

## Slide 29
Quantum computers provide massive speedup for problems in chemistry, material science, and machine learning
Quantum Computers enable solutions to important problems
Execution Time
Classical Computer
Problem Size
Quantum
Computer
100+ Years
Days
Potential of Quantum Computers
Efficient batteries
Efficient fertilizers
Zero-loss electric-grids
Notes: Why build quantum computers? So Quantum computing promise that we can solve problems which are unsolvable with todays computers, problems like molecular simulations
So how do quantum computer get this speedup? – So quantum computers leverage the properties of quantum bits to run extremely efficient quantum algorithms

## Slide 30: Quantum Bits
Quantum computer use quantum bits (qubits) to encode the information.
Classical Bit
Quantum Bit
State of a Classical Bit
 1 or 0 two points on sphere
State of a Quantum Bit
Any point on the sphere
Notes: Quantum

## Slide 31: Quantum Instruction: The Computing Model
Quantum Instructions manipulate the state of qubit
By rotating state vector in the Hilbert space
Quantum Instruction
Notes: To manipulate the state of qubit we can use quantum instructions. Which rotates the state vector from one point on the sphere to other point on the sphere.

## Slide 32: Transformation: The Key to Computing
Problem
Algorithms
PL & Compilers
Architecture
Devices/Technology
Circuits
Electrons
My proposal focuses on architecture for quantum computer
Problem
Quantum Algorithms
Compilers
Quantum Architecture
Quantum Interfaces
Quantum Devices
Photons/Ions/Superconductor
Notes: That’s why we want to do quantum architecture – to estimate what are the challenges and how w can make our systems more efficient and reliable

## Slide 33: Existing Superconducting Qubit Chips
5 Qubits
16 Qubits
20 Qubits
7 Qubits
17 Qubits
50 Qubits
IBM
Intel
In this proposal, I will focus on superconducting qubit technology

## Slide 34: Quantum Control Computer
Control Computer -- Interface between Qubits & Programmer
Quantum Computer = Qubits + Control Computer
Control Computer -- manipulates the qubit states
Control Computer
Qubits
Notes: Control computer executes instructions on a quantum computer

## Slide 35: Existing Quantum Computers
Qubits require cryogenic operating temperature to minimize thermal noise
Qubits
(20 mK)
Dilution Refrigerator
Quantum Bit
Qubits
Dilution Refrigerator
Ref: IBM Quantum Experience
Quantum Chip
Control Processor
Programmer
Source: IBM Quantum Experience
20 mK

## Slide 36: Quantum bits are fickle
Need Error Correction to protect Quantum bits
Even at 20mK, qubits can lose state
1
0
Classical Bit
Quantum Bit
Notes: Brief mention of decoherence

## Slide 37: Quantum Error Correction
Quantum Error Correction Code
Collection of Noisy
Physical Qubit Devices
Fault-Tolerant
Logical Qubit
Error Correction can enable Fault-tolerant Quantum Computers (FTQC)
QEC require 10 to 100 physical qubits to create fault-tolerant logical qubit

## Slide 38: Quantum Error Correction is Expensive
Quantum Error Correction require 10 to 100 physical qubits to create fault-tolerant logical qubit
For near-term we may have to use Noisy Intermediate Scale Quantum Computers (NISQ)
Near term quantum computers will be noisy
2010
2020
Future
2000
106
105
104
103
102
101
100
Noisy Intermediate Scale Quantum Computers
(NISQ)
FTQC
Number of demonstrated qubits

## Slide 39: Quantum Error Correction
Syndrome Generator
Syndrome Measurement
Data Qubits
Ancilla
Qubits
QECC is applied on all qubits continuously to preserve state
Fault-Tolerant
Logical Qubit
Notes: 1 min
Ancilla qubits
Entanglement
Diagram

## Slide 40: Cryogenic Control Processor
Cryogenic Control Processor is essential for scalable Quantum Computer
(Ref: Cryogenic Control Architecture for Large-Scale Quantum Computing by Hornibrook et. al)
Control Processor
Qubits
20mK
300K
Metal Wires
 Thermal Leakage
Qubits
20mK
Control Processor
Superconducting wires
 Low Leakage
4K

## Slide 41
Taming the Instruction Bandwidth of Quantum Computers
Swamit Tannu
Zach Myers
Prashant Nair
Douglas Carmean
Moinuddin Qureshi
(MICRO – 50)
Notes: 30 sec – cryogenic and quantum error correction

## Slide 42: QECC aware Control Architecture
Qubits
Control Processor
Uncorrectable Errors !!
FTQC  QEC instruction supply needs to scale linearly with number of qubits

## Slide 43: Programmable Quantum Error Correction
Different QECC Designed
New error correction codes  QECC needs to be programmable
Software managed QECC  Compiler inserts QECC instructions in regular instruction stream
Cost
Error Rate
Concatenation
Code
Surface
Code
Different Error Correction Designs
Programmable QEC is essential for leveraging trade-offs in QEC design
Notes: QECC is embedded in the programming model

## Slide 44: Problem: Instruction Bandwidth Bottleneck
Can’t use
i-cache
Can’t use i-cache -- delay in delivery of QECC instructions results in error
SW-QECC + no i-cache instruction bandwidth must scale linearly with number of qubits
Shor’s Algorithm
Instruction Bandwidth (B/s)
Total Bandwidth
Non-QECC Bandwidth
Number of Qubits
128 bit
256 bit
1024 bit
QECC Bandwidth Bloat – 10,000X
Notes: Hook for detailed discussion
Add more results

## Slide 45
Goal: To enable programmable Quantum Error Correction without bandwidth bloat
Programmability
BW Efficiency
Software-Managed QECC
Hardcoded
QECC

## Slide 46: Insight
QECC can be executed independently without any global synchronization
QECC is simple enough to manage in hardware using programmable microcode

## Slide 47: Quantum Error Correction Substrate (QuEST)
µcode engine continuously issues QECC µops
Master controller issues regular instructions. µcode Engine decodes it to µops
QuEST alleviates instruction bandwidth by issuing QECC ops locally
Master Controller
Control Processor
µ-Code
Engine
µ-Code
Engine
µ-Code
Engine
µ-Code
Engine
Qubits
Notes: Make baseline clear by animating the baseline– master controller sends both QECC and regular instructions
Thi

## Slide 48: QuEST -- Organization
Notes: 1.30 min

## Slide 49: Evaluations
QuEST reduces global bandwidth demand by orders of magnitude
Reduction in Global
Instruction Bandwidth
Chart: 
| BWT | BF | GSE | QLS | SHOR | TFP | GMEAN
 | 4.9 | 7.1 | 5.2 | 6 | 4 | 9.1 | 7.2
107x
105x
Notes: Why we get this benefit ?
Most of the instructions stem from QECC we handle QECC in microcode and that reduces the instruction bandwidth demand by several orders of magnitude. This graph shows Reduction in Global
Bandwidth demand on the y axis for quantum workloads including Shors algorithm.
On average Quest reduces instruction bandwidth demand by seven order of magnitude

## Slide 50: Key Takeaway for QUEST
Programmability
BW Efficiency
Software-Managed QECC
Hardcoded
QECC
QuEST (µcode)

## Slide 51: Scalable Organization

## Slide 52
Cryogenic DRAM based Memory System for Scalable Quantum Computers: A feasibility study
Swamit Tannu
Douglas Carmean
Moinuddin Qureshi
(MEMSYS 2017)
Notes: 30 sec

## Slide 53: Memory for Quantum Computers
Quantum Computer
Control Processor
Qubits
Memory
Data Memory
Program Memory
Quantum computers require substantial memory capacity at cryo temperature
Program Memory + Data Memory  Stores Quantum Executable , Data (~10s GB)
Memory must be kept at cryo temperature to avoid large thermal gradient
Josephson Junction technology works at 4K
 Limited memory density (only few Mb)
Notes: Quantum computer can be imagined as the conventional computer connected to the quantum bits or qubits . The conventional computer known as control processor which can manipulate the state of the qubits and act as an interface between the programmer and the qubits. Control processor requires memory to store the quantum program and store the quantum and classical variables. Quantum programs are large and require memory capacity of few 10s of GBs. On the other hand data memory is required to support quantum error correction which is fundamental to build a large scale quantum computers. Quantum error correction is necessary because qubits are fickle

## Slide 54
Does commodity DRAM work at cryogenic temperatures ?
Goal: To characterize a DRAM at cryogenic temperature to understand the functionality and error patterns
Notes: Skip THIS AND MOVE IT TO BACKUP

## Slide 55
Need mechanism to reduce DIMM temperature without affecting tester
Conventional memory testing  Memtest86 running on host, dedicated memory testers
Host machines or memory testers do not work at cryogenic temperatures
How to Test DRAM at Cryogenic Temperature?

## Slide 56: Isolated Cooling of DIMM
Need cryogenic coolant  Liquid Nitrogen (boils at 77K)
Need isolated cooling of DIMMs  Compact cryogenic heatsink
DIMM is sandwiched between two heatsinks and can be cooled down to 80K
Compact heatsink with Liquid Nitrogen provides isolated cooling of a DIMM

## Slide 58: Minimum Operational Temperature for DIMMs
18% DIMMs are functional below 90K
Chart: 
 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 81 | 87 | 94 | 98 | 99 | 100 | 101 | 103 | 104 | 107 | 107 | 109 | 112 | 112 | 112 | 113 | 113 | 113 | 114 | 116 | 116 | 116 | 117 | 119 | 119 | 120 | 120 | 121 | 121 | 121 | 123 | 123 | 123 | 123 | 125 | 126 | 129 | 130 | 132 | 132 | 132 | 135 | 137 | 138 | 153 | 162
Minimum Operating
Temperature (K)
DIMM Failure!
Notes: Title
Animation

## Slide 59: Chip Failures
92% of chips worked at 90K — Pick cryogenic tolerant chips
Chart: 
| Functional Chips | Faulty Chip
Faults | 690 | 60
92%
8%

## Slide 60: Fault Granularity
Uncorrelated faults  Conventional ECC can be effective for Cryo DRAM
Single bit errors  Uncorrelated faults
Linear codes (SECDED, BCH) are still effective
Single bit fault | 99.985%
Double bit fault | 0.015%

## Slide 61: Cold DRAM – Take Away
Quantum computers need dense memory at low temperature
Does DRAM Work at cryogenic temperature?
Experiments show  most commodity DRAM chips work at 90K
Error patterns are amenable to existing fault tolerance techniques

## Slide 62
Variation Aware Policies for NISQ-Era Quantum Computers
Swamit Tannu
Moinuddin Qureshi
(under review)
arXiv:1805.10224v1
Notes: 30 sec

## Slide 63: Programming Model for NISQ
Probability of successful trial (PST) is the key metric for NISQ machines
Execute instructions
1
Read qubit states
2
Repeat
Notes: NISQ machines do not have any protection against errors
NISQ programs also come in different flavors, there are programs which give answer in one trial
Whereas there are programs which require N trials
If ideal quantum computer that has no errors changes the trails substantially. Natutrally if you have errors then you need

## Slide 64: Data movement on quantum computer
A
B
C
D
E
Q1
Q2
Q3
cnot q[1], q[2];
cnot q[1], q[2];
swap q[2], q[3];
SWAP operations can be used to move data on a quantum computer

## Slide 65: Qubit Allocation Problem
A
B
C
D
E
cnot q[0], q[1];
cnot q[0], q[2];
cnot q[0], q[3];
cnot q[0], q[4];
#NISQ Program:
Mapping X
A  q [0]
B  q [1]
C  q [2]
D  q [3]
E  q [4]
Mapping Y
A  q [2]
B  q [1]
C  q [0]
D  q [3]
E  q [4]
Mapping | Total SWAPs
X | 1
Y | 
Qubit mapping has large impact on no. of swaps in NISQ applications
Mapping | Total SWAPs
X | 1
Y | 0
0
1
2
3
4
Mapping-X
1
2
0
3
4
Mapping-Y
cnot q[0], q[1];
cnot q[0], q[2];
cnot q[0], q[3];
cnot q[0], q[4];
#NISQ with Y:
cnot q[0], q[1];
swap q[0], q[2];
cnot q[0], q[2];
cnot q[0], q[3];
cnot q[0], q[4];
#Program with X:

## Slide 66: Cost of performing a SWAP operation
SWAP operations are unreliable
Extra SWAPs reduce reliability of applications significantly
Existing allocation policy [1] minimize number of SWAPs
[1] Alwin Zulehner, Alexandru Paler, and Robert Wille. Efficient mapping of quantum circuits to the ibm qx architectures (arXiv:1712.04722, 2017).
But allocation policy [1] use uniform SWAP cost

## Slide 67: Not all quantum links and qubits are created equal!
Characterization of IBM-Q20 show a heavy tail for link error rate
Link error rate over 52 days for 76 quantum links in IBM-Q20 machine

## Slide 68: Variation in Link Error Rates on IBM-Q20
All links are not created equal, IBMQ20 has significantly weak links
Average link error rate for 76 links in IBM-Q20 machine

## Slide 69
Goal: To improve reliability of NISQ by designing variation-aware compiler policies
Notes: Skip THIS AND MOVE IT TO BACKUP

## Slide 70
Q1
Q3
Q1
Q3
Q1
Q3
Q1
Q3
Qubit Movement Problem

## Slide 71: Variation-aware Qubit Movement (VQM)
Data Movement Path | Probability of Success
A-B-C-F | 0.8*0.8*0.6 = 0.384
Q1
Q3
0.8
0.8
0.9
0.7
0.6
0.6
0.8
cnot q[1], q[3]
Chose a sequence of swaps that maximizes the reliability
Data Movement Path | Probability of Success
A-B-C-F | 0.8*0.8*0.6 = 0.384
A-D-E-F | 0.8*0.7*0.6 = 0.336
Data Movement Path | Probability of Success
A-B-C-F | 0.8*0.8*0.6 = 0.384
A-D-E-F | 0.8*0.7*0.6 = 0.336
A-D-C-F | 0.8*0.9*0.8 = 0.576

## Slide 72: Variation-aware Qubit Allocation (VQA)
cnot q[1], q[2];
cnot q[2], q[3];
cnot q[3], q[4];
#NISQ Program:
Chose qubits that maximizes the reliability
0.8
0.8
0.9
0.7
0.6
0.6
0.8
Q4
Q1
Q3
Q2
Q4
PST1 = 0.43
PST2 = 0.57

## Slide 73: VQA and VQM Design
To enable VQA and VQM we use reliability-aware cost functions
For both VQM and VQA all the decisions are made using a greedy heuristic and they can be used with any existing allocation policies

## Slide 74: Impact of VQA+VQM on PST
VQA+VQM improves PST up to 1.83x over variation-unaware baseline
Notes: We build a simulator to evaluate the efficien

## Slide 75: Evaluations on IBM-Q5
Notes: We also test VQA and VQM on real machine

## Slide 76: Conclusion
Existing superconducting qubits suffer large variation in error-rate
Variation in error-rate can deteriorate the reliability of NISQ applications
Variation-aware policies for qubit allocation and movement can improve reliability by minimizing use of links that are significantly weak